## Slide 1: Liquid Silicon: A Data-Centric Reconfigurable Architecture Enabled by RRAM Technology
Yue Zha and Jing Li
Department of Electrical and Computer Engineering
University of Wisconsin-Madison
Feb 26, 2018

## Slide 2
Outline
Motivation
Background
Hardware Architecture
Circuit Implementation
CAD Tool Set
Evaluation

## Slide 3
Motivation
Machine Learning
Graph Analysis
Terabyte Sort
Datacenter/Cloud
Bioinformatics
Cybersecurity

## Slide 4
Motivation
Machine Learning
Graph Analysis
Terabyte Sort
Datacenter/Cloud
Bioinformatics
Cybersecurity
Search-intensive
Data-intensive
Large Problem Size
Limited on-chip storage (BRAM)
No support on native search function
Large routing overhead

## Slide 5
Motivation
Liquid Silicon – a Softer FPGA architecture
2D array of Tiles
Reconfigurable
Logic
Mode
Routing
Mode
Memory
Mode
Search
Mode
Configurable
Logic Block
Connection Block
Switch
Block
BRAM
?
One For All
Hard blocks
in FPGA
UltraRAM

## Slide 6
Motivation
Liquid Silicon – a Softer FPGA architecture
Compute Intensive
Search Intensive
Data Intensive
Fixed resource partition
CLB
BRAM
Logic
Mode
Memory
Mode
Search
Mode
Complement FPGA in search/data-intensive applications

## Slide 7
Background
Resistive Random-Access Memory (RRAM)
High
Resistance
State
Low
Resistance
State
Programmable
Ultra-dense crossbar
1D1R cell
Diode
RRAM
Mohammad, et al. (2016). State of the art of metal oxide memristor devices. Nanotechnology Reviews, 5(3), 311-329.

## Slide 8
Background
Resistive Random-Access Memory (RRAM)
Fackenthal, Richard, et al. "19.7 A 16Gb ReRAM with 200MB/s write and 1GB/s read in 27nm technology." 2014 IEEE International Solid-State Circuits Conference Digest of
Technical Papers (ISSCC). IEEE, 2014.
Liu, T., Yan, T., Scheuerlein, R., et al. (2013). A 130.7 mm2 2-Layer 32 Gb ReRAM Memory Device in 24 nm Technology. Proceedings of International Solid State Circuits
Conference (pp. 210–211).

## Slide 9
Hardware Architecture
Liquid Silicon – an RRAM-based reconfigurable architecture
2D array of Tiles
Crossbar
Connection Node
Connection
Node
Logic
Mode
Routing
Mode
Memory
Mode
Search
Mode
Reconfigurable
Notes: L-Si is one attempt to explore the potential of RRAM technology beyond storage.

## Slide 10
Hardware Architecture – Search Mode
Compare search key with stored words in parallel
Stored Word #0
Stored Word #1
Stored Word #2
Stored Word #3
Search Key
Match
Vector
One Tile
SRAM
SRAM
16 Transistors
CMOS-based design
~60 higher
storage
density
2 Cells
Notes: Our cad tool will optimize the orientation to improve the mapping quality

## Slide 11
Hardware Architecture – Search Mode
Stored Word #0
Stored Word #1
Stored Word #2
Stored Word #3
One Tile
SRAM
SRAM
16 Transistors
CMOS-based design
2 Cells
NW bits
BRAM
Search key as
memory address
Store match vector
FPGA-based design
Match
Vector
N2W bits
for N W-bit words
Better
Scalability
~60 higher
storage
density
Higher Update Cost
Compare search key with stored words in parallel
Notes: Our cad tool will optimize the orientation to improve the mapping quality

## Slide 12
Hardware Architecture – Search Mode
Stored Word #0
Stored Word #1
Stored Word #2
Stored Word #3
Store bit ‘1’
Store bit ‘0’
Store bit ‘X’
(Wildcard)
Two adjacent cells are encoded to store one bit
Connection node detects the leakage current
L
H
H
L
H
H
Search ‘0’
Search ‘1’
Search ‘1’
0
1
1
0
0
1
Mismatch
Turn on diodes

## Slide 13
Hardware Architecture – Search Mode
Stored Word #0
Stored Word #1
Stored Word #2
Stored Word #3
Store bit ‘1’
Store bit ‘0’
Store bit ‘X’
(Wildcard)
Two adjacent cells are encoded to store one bit
Connection node detects the leakage current
Search ‘1’
Search ‘0’
Search ‘1’
0
1
1
0
0
1
L
H
H
L
H
H
Match
Turn on diodes

## Slide 14
Logic Input
Hardware Architecture – Logic Mode
One tile implements a group of N-input Sum-of-Products
Logic Input
Logic
Output
One Tile
FPGA
Logic
Output
N-Input
M-Output
Sum-of-Products
N >> 6
6-Input LUT
6-Input LUT
6-Input LUT
Fine-grained logic
implementation
Coarse-grained logic
implementation
Shallower Logic Depth
Less Interconnections

## Slide 15
Hardware Architecture – Logic Mode
One tile implements a group of N-input Sum-of-Products
  Program RRAM cells into LRS to connect logic inputs
F = ABD
One Tile
0
1
0
1
False
L
H
L
L
F = A+B+D
Turn on diodes

## Slide 16
Hardware Architecture – Logic Mode
One tile implements a group of N-input Sum-of-Products
  Program RRAM cells into LRS to connect logic inputs
F = ABD
One Tile
1
1
0
1
True
L
H
L
L
Turn on diodes

## Slide 17
Hardware Architecture – Routing Mode
A special case of logic mode
  F = C
Co-exist with logic mode in the same tile
F = ABD
One Tile
Route C
Route Signal C
H
L
H
H

## Slide 18
Hardware Architecture – Routing Mode
A special case of logic mode
  F = C
Co-exist with logic mode in the same tile
Resources used for logic
Resources used for routing
F = ABD
One Tile
Flexible
Partition
CLB
CB
SB
Fixed partition
in FPGA
Route Signal C
Routing
Logic

## Slide 19
Hardware Architecture – Memory Mode
Four adjacent tiles to implement a memory block
Logic Mode
(e.g. Decoding Circuits)
Memory
Array

## Slide 20
Hardware Architecture – Memory Mode
Provided several flexibilities
  Flexible position/capacity
  Flexible logic aspect ratio
Tile configured
in Memory mode
FPGA
BRAMs in fixed columns

## Slide 21
Circuit Implementation
Key building blocks of connection nodes
S/A
Configurable
Dynamic
Inverter
Skippable
DFF/NOT
Voltage
Driver
Configuration
Memory

## Slide 22
Circuit Implementation – S/A
Two-stage sensing scheme
Low power consumption – limited precharge voltage
WL/BL
S/A
Configurable
Dynamic
Inverter
Skippable
DFF/NOT
Voltage
Driver
Configuration
Memory

## Slide 23
Circuit Implementation – Dynamic Inverter
Implement a multi-input dynamic NOR gate
Vdd
Sensing
Clock
Input
Controlled by
configuration
memory
S/A
Configurable
Dynamic
Inverter
Skippable
DFF/NOT
Voltage
Driver
Configuration
Memory
Vdd
Sensing
Clock
IN0
IN1
Sensing
Clock
Vdd
Out

## Slide 24
Improve resources utilization
  Sum-Of-Products
  The input of the OR function is rarely used by other functions
G
High Utilization
Low Utilization
Cannot map other
logic functions
Program RRAM into LRS
Circuit Implementation – Dynamic Inverter

## Slide 25
Circuit Implementation – Voltage Driver
Low Voltage Domain
Provides voltage for
Search/Logic/Routing Modes
High Voltage Domain
Provides voltage for
programming RRAM in
Memory Mode
S/A
Configurable
Dynamic
Inverter
Skippable
DFF/NOT
Voltage
Driver

## Slide 26
Circuit Implementation - Configuration Memory
3D2R Cell
Non-volatile
Organized in Crossbar
S/A
Configurable
Dynamic
Inverter
Skippable
DFF/NOT
Voltage
Driver
Configuration
Memory

## Slide 27
CAD Tool Set
Adapted from VTR project1
Use our custom place & route tool2
  Partition the hardware resources between four modes
2Zha, Yue, and Jing Li. "Reconfigurable in-memory computing with resistive memory crossbar." ICCAD. ACM, 2016.
1Luu, Jason, et al. "VTR 7.0: Next generation architecture and CAD system for FPGAs.” TRETS 7.2 (2014): 6.
FPGA
Liquid
Silicon
Less Routing Overhead

## Slide 28
1Luu, Jason, et al. "VTR 7.0: Next generation architecture and CAD system for FPGAs.” TRETS 7.2 (2014): 6.
CAD Tool Set
Adapted from VTR project1
Use our custom place & route tool2
  Optimally partition the hardware resources among four modes
2Zha, Yue, and Jing Li. "Reconfigurable in-memory computing with resistive memory crossbar." ICCAD. ACM, 2016.
FPGA
Liquid
Silicon
Flexible Memory

## Slide 29
Evaluation - Setup
Complete the physical design of Liquid Silicon
  Obtain the tile area
The physical design of one tile
Connection nodes are fully buried under the RRAM crossbar

## Slide 30
Evaluation - Setup
HSPICE simulation to obtain the delay and power
  Roff/Ron = 150kΩ/1kΩ
  Simulate different input/store patterns, PVT variation
Our CAD Tool is used to map applications onto Liquid Silicon
VTR is used to map applications onto FPGAs

## Slide 31
Evaluation - Setup
Four architectures include in the comparison
SRAM-based FPGA
(baseline)
RRAM-based FPGA
SRAM-based
Liquid Silicon
RRAM-based
Liquid Silicon
(proposed)
FPGA
Liquid Silicon
SRAM
RRAM
Architectural
Comparison
Technology
Comparison

## Slide 32
Evaluation – Logic Only
Evaluate the Logic/Routing modes
MCNC benchmark set
Area reduces 62%
Delay reduces 27%
Energy efficiency improves 31%
Better performance compared with SRAM-based FPGA

## Slide 33
Evaluation – Logic Only
Area reduces 26%
Delay reduces 37%
Energy efficiency improves 15%
Evaluate the Logic/Routing modes
MCNC benchmark set
Compare with RRAM-based FPGA
Improvement from architecture

## Slide 34
Evaluation – Logic Only
Evaluate the Logic/Routing modes
MCNC benchmark set
Routing area reduces 64%
Routing delay reduces 17%
Less routing overhead from
coarse-grained logic implementation
flexible resource partition

## Slide 35
Evaluation – Memory Evaluation
Evaluate the Memory/Logic/Routing Modes
Benchmarks from VTR project
Large-Memory
Utilize > 30% resources for memory
Small-Memory
Utilize < 30% resources for memory

## Slide 36
Evaluation – Memory Evaluation
Evaluate the Memory/Logic/Routing Modes
Benchmarks from VTR project
  Area reduce by 64%
  Delay decrease by 29%
  Energy efficiency improve by 65%
Better Performance
Larger Memory, Better Performance
Large-Memory
Small-Memory

## Slide 37
Evaluation – Search Evaluation
Packet classification – Networking Domain
Packet classification1
  Reduces area by 99%
  Reduces power by 94%
  Improves throughput by 30%
1W. Jiang. 2013. Scalable Ternary Content Addressable Memory implementation using FPGAs. In ANCS. 71–82
BRAM
Search key as
memory address
Store match vector
FPGA-based Design
Match
Vector
Software Defined Network
Programmable devices in UADP from Cisco
Notes: CISCO

## Slide 38
Evaluation – Search Evaluation
Join operation – Big Data Analysis
  Compare with hashing-based implementation
  Reduce the requirement on storage by 24%
  Improve the frequency by 50%
Francisco, P. (2014). Ibm puredata system for analytics architecture. IBM Redbooks, 1-16.
FPGAs in IBM’s Netezza

## Slide 39
Summary
Liquid Silicon – a Softer FPGA architecture
  Complement FPGA in data-/search-intensive applications
Provide circuit implementation and custom CAD tool
Improvement is not only from the advanced NVM technology
Data-/Search-Intensive
Large Problem Size
Liquid
Silicon

## Slide 40
Thank you!
This work is conducted under
DARPA Young Faculty award program
Notes: Darpa logo