## Slide 1: A Scalable Approach to Exact Resource-Constrained Scheduling Based on a Joint SDC and SAT Formulation
Steve Dai, Gai Liu, Zhiru Zhang
Electrical and Computer Engineering, Cornell University

## Slide 2: High-Level Synthesis (HLS)
Promising tool to reduce the development time for FPGA-targeted hardware designs
  Raises the level of design abstraction from hardware to software
  Tackles increased design complexity and stringent design constraints
Untimed
Timed
High-level
Software
Cycle-accurate
Hardware
Software Compilation
Scheduling
Binding
RTL Generation
C/C++/
SystemC
Adding timing information
Verilog/
VHDL

## Slide 3: Scheduling is Important
Timing influences the quality of the resulting hardware
  Enable micro-architectural tradeoffs from a single design source
Untimed | Combinational for Latency | Sequential for Area | Pipelined for Throughput
+
+
in
+
out
+
+
in1
+
out1
in2
in3
in4
+
+
in1
+
out1
in2
in3
in4
3
2
1
4
3
2
1
2
1
in1
+
out1
in2
in3
in4
REG
Control-Data Flow Graph (CDFG)

## Slide 4: HLS Scheduling with Constraints
Determines the clock cycle at which each operation should be executed subject to constraints
  Dependence
  Cycle time
  Relative timing
Resource-constrained scheduling
  Minimizes latency given a limited number of functional units
  Considers resource constraints in addition to other constraints
  NP-hard problem

## Slide 5: Tension between Scalability and Quality
High
scalability
(greedy
decisions)
High quality
(global optimization)
Low
quality
Slow
runtime
List scheduling
(e.g., [Parker et al., DAC’86])
Force-directed
[Paulin & Knight, TCAD’89]
Faster
Better QoR
ILP
SDC
(e.g., [Cong & Zhang, DAC’06])
?
Optimal quality
Fast runtime

## Slide 6: SDC-Based Scheduling
SDC = System of difference constraints
Target cycle time: 5ns
Delay estimates
  Add (+) 1ns
  Load (ld) 3ns
  Store (st) 1ns
si : schedule variable for operation i
Dependence constraints
      <v0 , v4 > : s0 – s4 ≤ 0
      <v1 , v3 > : s1 – s3 ≤ 0
      <v2 , v3 > : s2 – s3 ≤ 0
      <v3 , v4 > : s3 – s4 ≤ 0
      <v4 , v5 > : s4 – s5 ≤ 0
Cycle time constraints
v2  v5 : s2 – s5 ≤ -1
v1  v5 : s1 – s5 ≤ -1
[J. Cong & Z. Zhang, DAC, 2006] [Z. Zhang & B. Liu, ICCAD, 2013]
ld
+
ld
ld
+
v1
v3
v4
v2
v0
1ns
3ns
1ns
st
v5
1ns
Timing constraints

## Slide 7: SDC is Efficient
Difference constraints in a constraint graph
  Feasible (integer) schedule from single-source shortest path
  Detect infeasibility by the presence of negative cycle
Dependence constraints
      <v0 , v4 > : s0 – s4 ≤ 0
      <v1 , v3 > : s1 – s3 ≤ 0
      <v2 , v3 > : s2 – s3 ≤ 0
      <v3 , v4 > : s3 – s4 ≤ 0
      <v4 , v5 > : s4 – s5 ≤ 0
Cycle time constraints
v2  v5 : s2 – s5 ≤ -1
v1  v5 : s1 – s5 ≤ -1
s0
s1
s2
s3
s4
-1
s5
-1
0
0
0
0
0
-1
v4  v3 : s4 – s3 ≤ -1
Negative cycle = Certificate of infeasibility
[J. Cong & Z. Zhang, DAC, 2006] [Z. Zhang & B. Liu, ICCAD, 2013]
src
3
3
3
2
3
2
3
Feasible
schedule

## Slide 8: Resource Constraints in SDC
Cannot be represented exactly in integer difference form
Must be heuristically transformed into difference constraints
Resource constraints
 Heuristic partial orderings
v0  v2 : s0 – s2 ≤ -1
OR
v1  v0 : s1 – s0 ≤ -1
v2  v0 : s2 – s0 ≤ -1
3 cycle latency
2 cycle latency
ld
+
ld
ld
+
v1
v3
v4
v2
v0
1ns
3ns
1ns
st
v5
1ns
Resource constraint
  Two read ports
For scalability, SDC heuristically imposes one ordering
without guarantee of optimality
[J. Cong & Z. Zhang, DAC, 2006] [Z. Zhang & B. Liu, ICCAD, 2013]
Need to enumerate for best latency

## Slide 9: SDS: Exact Scheduling with SDC and SAT
Conflict based search
Graph based
feasibility checking
Polynomial time
~1M variables
>1M clauses
SAT
Resource Constraints
Partial orderings
Difference constraints
      s0 – s4 ≤ 0
      s1 – s3 ≤ 0
      s2 – s3 ≤ 0
      s3 – s4 ≤ 0
      s4 – s5 ≤ 0
s2 – s5 ≤ -1
s1 – s5 ≤ -1
SDC
Timing Constraints
Infeasibility
Conflict clauses
Conflict-driven learning
Satisfiability (SAT): Is there an assignment of the (Boolean) variables that satisfies a Boolean formula?
Still NP-hard, but optimal scheduling

## Slide 10: Resource Constraints in SAT
Boolean variables
  Bik Binding: i bound to resource k
  Rij Sharing: i shares resource with j
  Oij Partial ordering: i scheduled in an earlier cycle than j
SAT clauses for resource constraints
  Partial ordering constraint: If i and j share the same resource, they must be scheduled in different cycles

## Slide 11: Conflict-Driven Learning
Partial orderings
Difference constraints
Infeasibility
Conflict clauses
Is latency = 2 cycles feasible?
1
-1
-1
-1
propose
conflict
Negative cycle
sum = -1
s0
s1
s2
s3
s4
-1
s5
-1
What SAT learns from SDC:
Any ordering involving operation 0 before 2 should no longer be attempted

## Slide 12: Conflict-Driven Learning
Is latency = 2 cycles feasible?
1
propose
conflict
Negative cycle
sum = -2
s0
s1
s2
s3
s4
-1
s5
-1
-1
-1
-1

## Slide 13: Conflict-Driven Learning
Is latency = 2 cycles feasible?
1
propose
No conflict
No negative cycle
s0
s1
s2
s3
s4
-1
s5
-1
-1
-1
Feasible! Returns schedule.
Any ordering satisfying these conflicts are infeasible

## Slide 14: Fast Conflict-Driven Learning
Generate short conflicts
  Shorter conflict  more pruning  faster convergence
  Negative cycle = irreducibly inconsistent set of constraints
    Keeps conflicts short
    Becomes consistent if any constraint is removed from the set
  Resource-aware lower bounding [Rim & Jain, TCAD 1997]
    Complements negative cycle for conflict generation
    Can generate even shorter conflicts in certain cases

## Slide 15: Fast Incremental Learning
1
1
1
0
0
1
-1
0
s0
s1
s2
s3
s4
-1
s5
-1
0
Not necessary to process entire graph each time
  With incremental SDC, add edges only up until the constraint graph becomes infeasible
Incremental SDC [Ramalingam et al., Algorithmica 1999]
  Start with a feasible solution
  Add or tighten an edge
    O(|Δe|+ |Δv|log|Δv|)
    Update only affected subgraph
  Delete or relax an edge
    O(1)
    Current solution remains feasible

## Slide 16: Fast Incremental Learning
Incremental resource constraints
  Start with no resource constraints
  Add resource constraints only as needed to deal with contention
  Significantly reduce search space
    R01 → ( O01 ∨ O10 )
    ¬( O01 ∧ O10 )
    R02 → ( O02 ∨ O20 )
    ¬( O02 ∧ O20 )
    R12 → ( O12 ∨ O21 )
    ¬( O12 ∧ O21 )
    R01 → ( O01 ∨ O10 )
    ¬( O01 ∧ O10 )
    R02 → ( O02 ∨ O20 )
    ¬( O02 ∧ O20 )
s0
s1
s2
s3
s4
s5
    R01 → ( O01 ∨ O10 )
    ¬( O01 ∧ O10 )
    R02 → ( O02 ∨ O20 )
    ¬( O02 ∧ O20 )
    R12 → ( O12 ∨ O21 )
    ¬( O12 ∧ O21 )
    R01 → ( O01 ∨ O10 )
    ¬( O01 ∧ O10 )
    R02 → ( O02 ∨ O20 )
    ¬( O02 ∧ O20 )
    R01 → ( O01 ∨ O10 )
    ¬( O01 ∧ O10 )
    R12 → ( O12 ∨ O21 )
    ¬( O12 ∧ O21 )
SAT
Resource Constraints
SDC
Timing Constraints

## Slide 17: From Feasibility to Optimality
SAT is a decision problem
  How to optimize for latency?
Binary search over feasible latency range
  Automatically establish “tight” upper and lower bounds
latency
Lower
Bound
Upper
Bound
SDC
[Cong & Zhang,
DAC 2006]
Resource-aware
Lower Bounding
[Rim & Jain, TCAD 1997]
SDS handles constraints exactly and achieves optimal solution like ILP

## Slide 18: Implementation
SDS
C++
Lingeling SAT
C Compiler (LLVM)
Scheduling
Binding
RTL Generation
C Program
Synthesizable Verilog
Allocation
Target H/W
Characterization
User constrains
Timing
Resource
Optimized
LLVM IR
http://legup.eecg.utoronto.ca
LegUp HLS Flow
Constraints
Schedule

## Slide 19: Quality of Results
Dataflow benchmarks
  Contain a large portion of resource-constrained operations
  Stress-test scheduler’s resource handling capability
Benchmark | #Ops | SDS Latency | ILP Latency | SDC Latency
ARAI | 44 | 8 | 8 | 9
PR | 52 | 12 | 12 | 14
WANG | 54 | 12 | 12 | 14
LEE | 58 | 12 | 12 | 14
MCM | 74 | 15 | 15 | 16
DIR | 76 | 14 | 14 | 15
HONDA | 105 | 27 | 27 | 33
CHEM | 349 | 85 | Timeout | 89
U5ML | 857 | 261 | 261 | 264
Resource Constraints: 2 multipliers and 2 memory ports. Latency in cycles.
Timeout after 300 seconds.

## Slide 20: Runtime Results
Benchmark | # Operations | SDS Scheduling | Default ILP Scheduling | 
 |  |  | CPLEX | CBC
ARAI | 44 | 0.01 | 0.12 | 1.18
PR | 52 | 0.01 | 0.86 | 3.70
WANG | 54 | 0.01 | 0.86 | 12.2
LEE | 58 | 0.01 | 0.26 | 2.88
MCM | 74 | 0.34 | 6.19 | 24.6
DIR | 76 | 0.01 | 1.51 | 11.5
HONDA | 105 | 0.02 | 9.06 | 104
CHEM | 349 | 1.42 | TO | TO
U5ML | 857 | 0.01 | 20.8 | TO
Resource Constraints: 2 multipliers and 2 memory ports.
Runtimes in seconds.
Timeout after 300 seconds.
12x
86x
86x
26x
18x
151x
453x
Timeout
2080x
118x
370x
1220x
288x
72x
1150x
5200x
Timeout
Timeout
SDS Speedup over

## Slide 21: Runtime Results
The solver remains scalable for more resources
Benchmark | # Operations | SDS Scheduling |  |  |  | 
 |  | 1 mult 1 port | 2 mults 2 ports | 3 mults 3 ports | 4 mults 4 ports | 6 mults 6 ports
ARAI | 44 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01
PR | 52 | 0.01 | 0.01 | 0.01 | 0.01 | 0.02
WANG | 54 | 0.01 | 0.01 | 0.01 | 0.01 | 0.02
LEE | 58 | 0.01 | 0.01 | 0.01 | 0.01 | 0.02
MCM | 74 | 0.05 | 0.34 | 0.01 | 0.13 | 0.07
DIR | 76 | 0.02 | 0.01 | 0.01 | 0.01 | 0.01
HONDA | 105 | 0.01 | 0.03 | 0.04 | 0.09 | 0.24
CHEM | 349 | 1.49 | 1.42 | 1.10 | 2.92 | 4.33
U5ML | 857 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01
Runtimes in seconds.

## Slide 22: Additional Results
CHStone benchmarks
  Target Intel Cyclone V FPGA at 10ns
  Both SDC and SDS can schedule within 50ms
Benchmark | #Ops | SDC-Based Scheduling |  |  | SDS Scheduling |  | 
 |  | CP | ALM | #Control Steps | CP | ALM | #Control Steps
ADPCM | 850 | 12.0 | 5599 | 95 | 11.3 | 5680 | 86
AES | 812 | 10.4 | 5313 | 174 | 10.5 | 5506 | 167
BLOWFISH | 687 | 7.5 | 2209 | 110 | 7.8 | 2402 | 106
DFMUL | 279 | 9.4 | 1112 | 7 | 9.6 | 1126 | 6
DFADD | 361 | 7.3 | 1439 | 8 | 7.4 | 1442 | 8
DFSIN | 1067 | 10.2 | 8584 | 78 | 9.6 | 8541 | 78
GSM | 966 | 10.2 | 3256 | 7 | 10.6 | 3233 | 7
MIPS | 346 | 11.7 | 1036 | 5 | 11.8 | 1029 | 5
MOTION | 284 | 8.4 | 5577 | 11 | 9.0 | 5729 | 11

## Slide 23: Take-Away Points
Combine SDC and SAT with conflict-driven learning to enable fast yet exact resource-constrained scheduling
Broader applications
  Not specific to HLS
  Resource-constrained scheduling in other fields
  Wide range of constrained scheduling problems
High Scalability
High Quality
SDC
SDS
Low Quality
Low Scalability

## Slide 24: Take-Away Points
Inspired by SMT (Satisfiability Modulo Theory)
  Leverage problem-specific knowledge to improve efficiency
  Use SAT solver only as a black box
Explore benefits of tightly integrating SDC with SAT in a more SMT-like approach
SAT
SDC
SAT
SDS++
Thank you! Questions?