## Slide 1: Accelerating Graph Analytics By Co-Optimizing Storage and Access on an FPGA-HMC Platform
Soroosh Khoram, Jialiang Zhang, Maxwell Strange, Jing Li
khoram@wisc.edu, jialiang.zhang@ece.wisc.edu, mbstrange@wisc.edu, jli@ece.wisc.edu
Department of Electrical and Computer Engineering
University of Wisconsin-Madison

## Slide 2: Agenda
Motivation and Background
Workload Characterization
Proposed Algorithm
Hardware Implementation
Evaluation
Conclusion

## Slide 3: Agenda
Motivation and Background
Workload Characterization
Proposed Algorithm
Hardware Implementation
Evaluation
Conclusion

## Slide 4: Motivation

## Slide 5: Motivation

## Slide 6: Graph Analytics Challenges
Large graph workloads present key challenges for processing systems
Poor locality
Abundant memory
accesses
Memory-bound

## Slide 7: Graph Analytics Challenges
Large graph workloads present key challenges for processing systems
Poor locality
Abundant memory
accesses
Memory-bound

## Slide 8: Breadth First Search
A ubiquitous building block for state-of-the-art graph analytics
Makes frequent random memory accesses.
1
4
3
2
5
6
7
8
9
10
11
1
4
3
2
5
6
7
8
9
10
11

## Slide 9: Breadth First Search
A ubiquitous building block for state-of-the-art graph analytics
Makes frequent random memory accesses.
1
4
3
2
5
6
7
8
9
10
11
1
4
3
2
5
6
7
8
9
10
11

## Slide 10: Breadth First Search
A ubiquitous building block for state-of-the-art graph analytics
Makes frequent random memory accesses.
1
4
3
2
5
6
7
8
9
10
11
1
4
3
2
5
6
7
8
9
10
11

## Slide 11: Breadth First Search
A ubiquitous building block for state-of-the-art graph analytics
Makes frequent random memory accesses.
1
4
3
2
5
6
7
8
9
10
11
1
4
3
2
5
6
7
8
9
10
11

## Slide 12: Previous Work
Previously we improved BFS by:
  Reducing unnecessary memory accesses
  Optimizing access granularity to memory
  Using Hybrid Memory Cube
Zhang et al. Boosting the Performance of FPGA-based Graph Processor using Hybrid Memory Cube: A Case for Breadth First Search, FPGA’17

## Slide 13: Hybrid Memory Cube
HMC is excellent for graph analytics and provides:
  High-speed, parallel random access
  Small access granularity
  Near-data processing

## Slide 14: Agenda
Motivation and Background
Workload Characterization
Proposed Algorithm
Hardware Implementation
Evaluation
Conclusion

## Slide 15: Workload Characterization
BFS is a memory-bound algorithm
Flag reads (flag R) make up the vast majority of the accesses
Flag reads are random and low-efficiency

## Slide 16: Agenda
Motivation and Background
Workload Characterization
Proposed Algorithm
Hardware Implementation
Evaluation
Conclusion

## Slide 17: Motivation
All vertices with flag reads might not fit together
This set can change depending on source vertex
1
4
3
2
5
6
7
8
9
10
11

## Slide 18: Key Insight
Flag reads happen to second-order neighbors simultaneously
1
4
3
2
5
6
7
8
9
10
11

## Slide 19: Algorithm Overview
Our clustering algorithm has three steps:
  Divide large graphs into subgraphs
  Generate Second-order neighbors subgraph (SONS)
  Cluster the SONS
Step 3
Step 2
SONS
Step 1

## Slide 20: Algorithm Overview
Our clustering algorithm has three steps:
  Divide large graphs into subgraphs
  Generate Second-order neighbors subgraph (SONS)
  Cluster the SONS
Step 1
Step 2
Step 3
SONS

## Slide 21: Step 1
Processing full graph is expensive and unnecessary
We used Markov algorithm for its robustness but it can be replaced with any other method.

## Slide 22: Step 2
Generate second-order neighbors subgraph:
  The same vertices
  Connects second-order neighbors in the original subgraph
Reveals groups of second-order neighbors

## Slide 23: Step 3
Group vertices of SONS into clusters to be stored in the same memory block.
We use a modified version of the RNSC clustering algorithm for this purpose.

## Slide 24: Agenda
Motivation and Background
Workload Characterization
Proposed Algorithm
Hardware Implementation
Evaluation
Conclusion

## Slide 25: Hardware Overview
Redirect flag reads to a merging unit that merges duplicate requests
It also caches the results for future requests

## Slide 26: Merging Unit
Scheduler redirects requests to their corresponding cache
Cache stores flag read results
Request tracker records requests waiting response

## Slide 27: Agenda
Motivation and Background
Workload Characterization
Proposed Algorithm
Hardware Implementation
Evaluation
Conclusion

## Slide 28: Setup
We use Xilinx KCU060 connected to a 4GB HMC
We use five parallel kernels

## Slide 29: Benchmarks
We used 10 graphs from the University of Florida Sparse Matrix Collection
Number of vertices from 450,000 to 1,700,000
Edge factors between 3 and 28

## Slide 30: Evaluation Results
Compare cache hit between clustered and unclustered graphs
Clustering improves cache hit by 3x on average

## Slide 31: Evaluation Results
Compare flag reads from the HMC between clustered and unclustered
Flag reads are reduced to 61% on average

## Slide 32: Evaluation Results
Merging alone (green bar) has little effect on performance
Merging + clustering (blue bar) improves performance by 2.8x on average

## Slide 33: Evaluation Results
We produce competitive results compared to state-of-the-art GPU
Overall 1.7x improvement
Results projected based on bandwidth

## Slide 34: Agenda
Motivation and Background
Workload Characterization
Proposed Algorithm
Hardware Implementation
Evaluation
Conclusion

## Slide 35: Conclusion
Improved graph traversal performance through software-hardware codesign
  Improved locality from the software
  Designed request merging support from the hardware
BFS performance improved by 2.8x
Provided competitive performance to state-of-the-art of GPU

## Slide 36: Thank You!
Notes: 36
36
36