## Slide 1: Stop Crying Over Your Cache Miss Rate: Handling Efficiently Thousands of Outstanding Misses in FPGAs
Mikhail Asiatici and Paolo Ienne
Processor Architecture Laboratory (LAP) School of Computer and Communication Sciences EPFL
February 26, 2019

## Slide 2: Motivation
DDR3-1600 Memory
Memory Controller
800 MHz DDR
200 MHz
Arbiter
Accelerator
Accelerator
0.8 GB/s
512
64
…
12.8 GB/s
32
12.8 GB/s
32
0.8 GB/s
0.8 GB/s
Blocking
Cache
Data blocks stored in cache, hoping for future reuse
Non-Blocking
Cache
FPGA
Memory
<<
<<
Reuse
Memory-level parallelism
Notes: FPGAs rely on massive datapath parallelism (1) to provide acceleration despite the frequency gap (2) with CPUs and GPUs. However, such parallelism is wasted if the memory system is unable to feed it. This is a problem whenever irregular accesses to external memory are common (3), and applications that do so often end up being memory bound. Let’s see why is it so and what we can do about it in the most general case.
Suppose we want to use a DDR3-1600 that operates at 800 MHz DDR (4). At 64 bits/transfer, it can provide up to 12.8 GB/s of bw (5). To expose the full bandwidth to the slower FPGA clock domain, the memory controller (6) will have a very wide memory interface – in this case, 512 bits (7). Now, if accelerators operate on narrow data (8), and their access patterns are not mutually correlated, or we can’t afford design effort figuring out how we can correlate them or make use of bursts, then sharing this memory channel efficiently is not trivial.
The simplest way to do so is by using an arbiter (9) that time-multiplexes this memory channel. While this allows us to maximize memory-level parallelism, fully pipelining memory access, we will never use more than 32 bits per cycle (10), that is, 1/16th of the bandwidth (11).
Another possibility would be to use a simple blocking cache (12). The cache would store data blocks, hoping for future reuse (13). However, whenever a miss occurs (14), the memory channel is stalled until the missing cache line returns from memory. If the memory has a 50-cycle latency, this means that there will have at most one transfer every 50 cycles (15). Therefore, unless the hit rate is very high, the bandwidth utilization will not be better than with an arbiter, possibly even worse.
A non-blocking cache (16) would do a better job. It is a cache, so it allows reuse of stored blocks (17), but misses will not prevent subsequent hits to be served, and it can tolerate a certain number of outstanding misses, which improves MLP (18). It looks like the ideal solution, right? The key is the number of outstanding misses that can be tolerated. Traditional non-blocking caches can tolerate a few tens of misses; however, if the hit rate is low and the memory latency is long, then even the non-blocking cache may stall too early, making it not too different from a blocking cache.
In this presentation, we will show that the mechanism used by non-blocking caches to keep track of outstanding misses not only increases MLP but also improves reuse (20) and that, if temporal locality is low, trading some or all the area used by the cache to keep track of more outstanding misses can increase performance (21).

## Slide 3: Motivation
Non-Blocking
Cache
Memory-level parallelism
Reuse
If hit rate is low, tracking more outstanding misses can be more cost-effective than enlarging the cache
Reuse

## Slide 4: Outline
Background on Non-Blocking Caches
Efficient MSHR and Subentry Storage
Detailed Architecture
Experimental Setup
Results
Conclusions
Notes: We’ll see how the implementation of standard non-blocking caches provides reuse of in-flight cache lines, then…

## Slide 5: Non-Blocking Caches
MSHR array
tag
subentries
0x1004
External memory
0x100
0x100C
miss
0x100
4
C
Cache array
tag
data
0x123
0xCA8
0x1F2D5D08706718799CD58F2F566
0xE9C0F7A7697CBA7CDC1A7934E34
0x100: 0x36C2156B751D4EBB940316495CB
0x156B
0xEBB9
Primary miss
allocate MSHR
allocate subentry
send memory request
Secondary miss
allocate subentry
MSHR = Miss Status Holding Register
0x100
0x36C2156B751D4EBB940316495CB
MSHRs provide reuse without having to store the cache line → same result, smaller area
More MSHRs can be better than a larger cache
Notes: When a non-blocking cache has a miss, instead of stalling like a blocking cache, it stores the miss information in an MSHR…
Stress that this is the standard non-blocking cache implementation
Explain that cache provides reuse for future, MSHRs while the cache line is in flight. If MSHR lifetime is long enough (long memory latency),

## Slide 6: Outline
Background on Non-Blocking Caches
Efficient MSHR and Subentry Storage
Detailed Architecture
Experimental Setup
Results
Conclusions

## Slide 7: How To Implement 1000s of MSHRs?
One MSHR tracks one in-flight cache line
MSHR tags need to be looked up
  On a miss: primary or secondary miss?
  On a response: retrieve subentries
Traditionally: MSHRs are searched fully associatively [1, 2]
  Scales poorly, especially on FPGAs
Set-associative structure?
[1] David Kroft “Lockup-free instruction fetch/prefetch cache organization” ISCA 1981
[2] K. I. Farkas and N. P. Jouppi “Complexity/Performance Tradeoffs with Non-blocking Loads” ISCA 1994
=
=
=
=
=
=
=
=
MSHR array
tag
subentries
Notes: Explain why fully associative scales poorly (area and delay for comparators and parallel lookup)

## Slide 8: Storing MSHRs in a Set-Associative Structure
Use abundant BRAM efficiently
0x87
0x46
0x10
0x24
2
0x59

## Slide 9: Storing MSHRs in a Set-Associative Structure
0x87
0x46
0x10
0xA3
4
0x24
0x59
Use abundant BRAM efficiently
Collisions?
  Stall until deallocation of colliding entry
→ Low load factor
(25% avg, 40% peak with 4 ways)
Solution: cuckoo hashing
Notes: Say that 25% and 40% come from our measurements

## Slide 10: Cuckoo Hashing
h0
hd-1
0x879
0x463
0x100
0x244
0x591
[3] A. Kirsch and M. Mitzenmacher “Using a queue to de-amortize cuckoo hashing in hardware” AACCCC 2007
0x463
0x463
Use abundant BRAM efficiently
Collisions can often be resolved immediately
  With a queue [3], during idle cycles
High load factor
  3 hash tables: > 80% average
  4 hash tables : > 90% average

## Slide 11: Efficient Subentry Storage
One subentry tracks one outstanding miss
Traditionally: fixed number of subentry slots per MSHR
  Stall when an MSHR runs out of subentries [2]
  Difficult tradeoff between load factor and stall probability
Decoupled MSHR and subentry storage
  Both in BRAM
Subentry slots are allocated in chunks (rows)
  Each MSHR initially gets one row of subentry slots
  MSHRs that need more subentries get additional rows, stored as linked lists
  Higher utilization and fewer stalls than static allocation
4
C
[2] K. I. Farkas and N. P. Jouppi “Complexity/Performance Tradeoffs with Non-blocking Loads” ISCA 1994
tag
subentries
tag
subentries
0x100

## Slide 12: Outline
Background on Non-Blocking Caches
Efficient MSHR and Subentry Storage
Detailed Architecture
Experimental Setup
Results
Conclusions

## Slide 13: MSHR-Rich Memory System General Architecture
Ni
Nb
tag
subentries
Notes: Say “it’s like a multibanked cache”

## Slide 14: Miss Handling
56 0x7362
ID
Address
miss

## Slide 15: Miss Handling
56 0x732
0x736
51
Pointer to first row of subentries
Notes: Say that I skip MSHR buffer for time reasons and rather spend more words on the subentry buffer

## Slide 16: Subentry Buffer
Subentry
buffer
rdaddr
rddata
wraddr
wrdata
Update logic
Response
generator
Free row queue (FRQ)
51
25 3
Head row from MSHR buffer
ID
Offset
56 2
51
25 3
56 2
25 3
0x736
51
tag
One read, one write per request: insertion pipelined without stall
(dual-port BRAM)
56 2
ptr
ID
offset
ID
offset
ptr

## Slide 17: Subentry Buffer
Subentry
buffer
rdaddr
rddata
wraddr
wrdata
Update logic
Response
generator
Free row queue (FRQ)
51
51
25 3
56 2
25 3
103
56 2
103
13 0
103
103
13 0
Stall needed to insert extra row
25 3
103
51
tag
56 2
ptr
ID
offset
ID
offset
ptr
13 0
ID
offset
ID
offset
ptr
0x736

## Slide 18: Subentry Buffer
Subentry
buffer
rdaddr
rddata
wraddr
wrdata
Update logic
Response
generator
Free row queue (FRQ)
25 3
103
56 2
A9 2
Linked list traversal: stall…
…only sometimes, thanks to last row cache
103
51
13 0
Last row cache
25 3
103
51
tag
56 2
ptr
ID
offset
ID
offset
ptr
13 0
ID
offset
ID
offset
ptr
0x736

## Slide 19: Subentry Buffer
Last row cache
Subentry
buffer
rdaddr
rddata
wraddr
wrdata
Update logic
Response
generator
Free row queue (FRQ)
51
51
25 3
103
56 2
1AF6
60B3
2834
C57D
Data from memory
25
56
C57D
2834
103
25 3
103
51
tag
56 2
ptr
ID
offset
ID
offset
ptr
13 0
ID
offset
ID
offset
ptr
0x736

## Slide 20: Subentry Buffer
Last row cache
Subentry
buffer
rdaddr
rddata
wraddr
wrdata
Update logic
Response
generator
Free row queue (FRQ)
1AF6
60B3
2834
C57D
C57D
2834
103
13 0
Stall requests only when
allocating new row
iterating through linked list, unless last row cache hits
a response returns
Overhead is usually negligible
13 0
ID
offset
ID
offset
ptr

## Slide 21: Outline
Background on Non-Blocking Caches
Efficient MSHR and Subentry Storage
Detailed Architecture
Experimental Setup
Results
Conclusions

## Slide 22: Experimental Setup
Memory controller written in Chisel 3
  4 accelerators, 4 banks
Vivado 2017.4
ZC706 board
  XC7Z045 Zynq-7000 FPGA with 437k FFs, 219k LUTs, 1090 18kib BRAMs (2.39 MB of on-chip memory)
  1 GB of DDR3 on processing system (PS) side – 3.5 GB/s max bandwidth
  1 GB of DDR3 on programmable logic (PL) side – 12.0 GB/s max bandwidth
f = 200 MHz
  To be able to fully utilize DDR3 bandwidth

## Slide 23: Compressed Sparse Row SpMV Accelerators
This work is not about optimized SpMV!
  We aim for a generic architectural solution
Why SpMV?
  Representative of latency-tolerant, bandwidth-bound applications with various degrees of locality
  Important kernel in many applications [5]
  Several sparse graph algorithms can be mapped to it [6]
[5] A. Ashari et al. “Fast Sparse Matrix-Vector Multiplication on GPUs for graph applications” SC 2014
[6] J. Kepner and J. Gilbert “Graph Algorithms in the Language of Linear Algebra” SIAM 2011
Notes: Don’t say: “change access pattern by changing sparsity”; rather say “by taking matrices from different domains, we can evaluate very different access patterns”

## Slide 24: Benchmark Matrices
matrix | non-zero elements | rows | vector size | stack distance percentiles 75% 90% 95% |  | 
dblp-2010 | 1.62M | 326k | 1.24 MB | 2 | 348 | 4.68k
pds-80 | 928k | 129k | 1.66 MB | 26.3k | 26.6k | 26.6k
amazon-2008 | 5.16M | 735k | 2.81 MB | 6 | 6.63k | 19.3k
flickr | 9.84M | 821k | 3.13 MB | 3.29k | 8.26k | 14.5k
eu-2005 | 19.2M | 863k | 3.29 MB | 5 | 26 | 69
webbase_1M | 3.10M | 1.00M | 3.81 MB | 2 | 19 | 323
rail4284 | 11.3M | 4.28k | 4.18 MB | 0 | 13.3k | 35.4k
youtube | 5.97M | 1.13M | 4.33 MB | 5.8k | 20.6k | 32.6k
in-2004 | 16.9M | 1.38M | 5.28 MB | 0 | 4 | 11
ljournal | 79.0M | 5.36M | 20.5 MB | 19.3k | 120k | 184k
mawi1234 | 38.0M | 18.6M | 70.8 MB | 20.9k | 176k | 609k
road_usa | 57.7M | 23.9M | 91.4 MB | 31 | 601 | 158k
> total BRAM size
Higher → poorer temporal locality
https://sparse.tamu.edu/

## Slide 25: Outline
Background on Non-Blocking Caches
Efficient MSHR and Subentry Storage
Detailed Architecture
Experimental Setup
Results
Conclusions

## Slide 26: Area – Fixed Infrastructure
 | Slices
Baseline with 4 banks | 11.0k
Our system with 4 banks | 10.0k
Baseline: cache with 16 associative MSHRs + 8 subentries per bank
  Blocking cache & no cache perform significantly worse
MSHR-rich: -10% slices
  MSHRs & subentries: FFs → BRAM
  < 1 % variation depending on MSHRs and subentries
What about BRAMs?
(4 accelerators + MIG: 11.9k)
Notes: All data from 16a on lappc14
Accelerators + DMAs + MIG + ROBs: 11452
Associative MHA (FPGAMSHR – ROBs): 10987
MSHR-rich (FPGAMSHR – ROBs): 9984

## Slide 27: BRAMs vs Runtime
Runtime (cycles/multiply-accumulate)
Area (BRAMs)

## Slide 28: BRAMs vs Runtime

## Slide 29: BRAMs vs Runtime

## Slide 30: BRAMs vs Runtime

## Slide 31: BRAMs vs Runtime

## Slide 32: BRAMs vs Runtime
25% faster, 24x fewer BRAMs
Same performance, 3.9x fewer BRAMs
6% faster, 2.4x fewer BRAMs
1% faster, 3.2x fewer BRAMs
7% faster, 2x fewer BRAMs
Same performance, 5.5x fewer BRAMs
6% faster, 2x fewer BRAMs
3% faster, 3.4x fewer BRAMs
6% faster, 2x fewer BRAMs
90% of Pareto-optimal points are MSHR-rich
25% are MSHR-rich with no cache!

## Slide 33: Outline
Background on Non-Blocking Caches
Efficient MSHR and Subentry Storage
Detailed Architecture
Experimental Setup
Results
Conclusions

## Slide 34: Conclusions
Traditionally: avoid irregular external memory accesses, whatever it takes
  Increase local buffering → area/power
  Application-specific data reorganization/algorithmic transformations → design effort
Latency-insensitive and bandwidth-bound? Repurpose some local buffering to better miss handling!
  Most Pareto-optimal points are MSHR-rich, across all benchmarks
  Generic and fully dynamic solution: no design effort required

## Slide 35: Thank you!
  https://github.com/m-asiatici/MSHR-rich

## Slide 36: Backup

## Slide 37: Benefits of Cuckoo Hashing
Achievable MSHR buffer load factor with uniformly distributed benchmark, 3x4096 subentry slots, 2048 MSHRs or closest possible value

## Slide 38: Benefits of Subentry Linked Lists
Subentry slots utilization
Subentry-related stall cycles
External memory requests
All data refers to ljournal with 3x512 MSHRs/bank

## Slide 39: Irregular, Data-Dependent Access Patterns: Can We Do Something About Them?
Case study: SpMV with pds-80 from SuiteSparse [1]
  Assume matrix and vector values are 32-bit scalars
  928k NZ elements
  129k rows, 435k columns → 1.66 MB of memory accessed irregularly
Spatial locality: histogram of reuses of 512-bit blocks
…but, hit rate with a 256 kB, 4-way associative cache
is only 66%! Why??
pds-80 as it is has essentially same reuse
opportunities as if it was scanned sequentially
[1] https://sparse.tamu.edu/

## Slide 40: Reuse with Blocking Cache
Four cache lines, LRU, fully-associative:
+1 cache line:
Eviction limits reuse window
  Mitigated by adding cache lines
Longer memory latency → more wasted cycles
time
time
speedup
M
M
M
M
M

## Slide 41: Reuse with Non-Blocking Cache
Four cache lines, LRU, fully-associative, one MSHRs:
Four cache lines, LRU, fully-associative:
time
time
MSHRs widen reuse window
Fewer stalls, wasted cycles less sensitive to memory latency
In terms of reuse, if memory has long latency, or if it can’t keep up with requests, 1 MSHR ≈ 1 more cache line
  1 cache line = 100s of bits
  1 MSHR = 10s of bits
speedup
→ Adding MSHRs can be more cost-effective than enlarging the cache, if hit rate is low
M
M
M
M
M
M
M

## Slide 42: Stack Distance
Stack distance: #different blocks referenced between to references to the same block
{746, 1947, 293, 5130, 293, 746}
4,096
(256 kB cache)
Always a miss
Always a hit
Can be a hit
S = 1
S = 3
Temporal locality: cumulative histogram of stack distances of reuses
Fully associative, LRU cache
Realistic cache

## Slide 43: Harnessing Locality With High Stack Distance
Cost of shifting the boundary by one: one cache line (512 bit)
  Is there any cheaper way to obtain data reuse, in a general case?
4,096
(256 kB cache)
Always a miss
Can be a hit

## Slide 44: MSHR Buffer
Request pipeline must be stalled only when:
  Stash is full
  A response returns
Higher reuse → fewer stalls due to responses

## Slide 45: Memory-Bound Applications
FPGAs rely on massive datapath parallelism to overcome frequency gap with CPUs and GPUs
Wasted if memory system is unable to feed it
Not a problem if:
  Dataset is small enough to fit into on-chip RAM
  High computational intensity
  Accesses are sequential → efficient burst reads
  Accesses are regular → scratchpads
  Accesses have spatial and temporal locality → caches
  Access pattern is known at compile-time → data reorganization, memory banking

## Slide 46: Irregular, Data-Dependent Access Patterns
What if
  Access pattern has poor locality, is irregular and data-dependent (e.g. sparse linear algebra and graph analytics)?
  Design effort for an application-specific solution is not an option?
Maximize MLP: emit enough outstanding memory requests to fully exploit memory latency
Still, throughput limited to one memory operation per cycle per channel
If accelerators have narrow data ports, memory bandwidth can be significantly underutilized