## Slide 1: Improving Performance of Graph Processing on FPGA-DRAM Platform by Two-level Vertex Caching
Zhiyuan Shao, Ruoshi Li, Diqing Hu, Xiaofei Liao, and Hai Jin
School of Computer Science and Technology
Huazhong University of Science and Technology

## Slide 2: Outline
Background and Motivation
Our Solution: FabGraph
Tech. details
Evaluation
Conclusion and Future Work

## Slide 3: Large-scale Graph Processing
Extensively used in various domains
High memory-accessing/computing ratio

## Slide 4: FPGA Memory Hierarchy

## Slide 5: ForeGraph (state-of-art system)
Graph representation
  2-Dimensional grid
  irregular→ regular

## Slide 6: ForeGraph (state-of-art system)

## Slide 7: ForeGraph (state-of-art system)
Problems
  Frequent pipeline stalls caused by vertex data exchanging with DRAM
  Edge inflation problem (11% to 34%)

## Slide 8: Outline
Background and Motivation
Our Solution: FabGraph
Tech. details
Evaluation
Conclusion and Future Work

## Slide 9: System overview (FabGraph)
Basic idea
  2-level vertex caching
With it, we can…
  Reduce data transmissions between DRAM and FPGA
  Overlap communication with computation
  Eliminate/reduce pipeline stalls
  Solve the edge inflation problem

## Slide 10: Outline
Background and Motivation
Our Solution: FabGraph
Tech. details
  L2 cache data replacement
  Communication/Computation overlapping
  Space allocation for two cache levels
  Enhanced pipelines
Evaluation
Conclusion and Future Work

## Slide 11: L2 cache data replacement
Hilbert order-like replacement
 | ForeGraph | FabGraph | 
 |  | SL2 < Q | SL2 ≥ Q
Read | Q+Q2/K | Q2/SL2-(Q-SL2)/2 | 0
Write | Q2/K | Q2/SL2-(Q-SL2)/2 | 0
Now we have: Q=8, SL2=K=4
(ForeGraph) Read: 24 /Write: 16 (vertex intervals)
(FabGraph) Read: 14 /Write: 14 (vertex intervals)

## Slide 12
Communication/Computation overlapping

## Slide 13: Communication/Computation overlapping (Cont’d)
Overlapping factor:
α=Tactual/Ttheory
α=1: perfect overlapping
α>1: imperfect overlapping

## Slide 14: Space allocation for two cache levels
Case 1: boards with BRAM+URAM (URAM is larger than BRAM)
  Use BRAM as the L1 cache
  Use URAM as the L2 cache

## Slide 15: Space allocation for two cache levels (Cont’d)
Case 2: boards with BRAM only
  Allocate BRAM space for both L1 and L2 cache
Assume Q = 74, Mbram = 64, |E| = 69M, α = 1, BWdram = 19.2GB/s, Fpipe (enhanced) = 150MHz
Assume Q = 74, |E| = 69M, BWdram = 19.2GB/s, α = 1, and Fpipe(enhanced) = 150MHz

## Slide 16: Enhanced pipelines

## Slide 17: Outline
Background and Motivation
Our Solution: FabGraph
Tech. details
Evaluation
Conclusion and Future Work

## Slide 18: Evaluation Setup
Platform
  Xilinx Virtex UltraScale VCU110 (16.61MB BRAM)
  Xilinx Virtex UltraScale+ VCU118 (9.48MB BRAM + 33.75MB URAM)
  Xilinx Vivado 2017.4 (simulation)
  DRAM peak bandwidth: 19.2GB/s (DRAMSim2)
Datasets
Graphs | #vertices | #edges | Q
Com-Youtube (YT) | 1.13 million | 2.99 million | 18
SOC-Pokec (PK) | 1.63 million | 30.62 million | 26
Wiki-Talk (WK) | 2.39 million | 5.02 million | 38
Soc-LiveJournal (LJ) | 4.85 million | 68.99 million | 74

## Slide 19: Evaluation on VCU110
Algorithm | Graph | BRAM | SL1 (MB) | SL2 (MB) | #pipelines | LUT | FF | Fpipe (MHz) | Fbram (MHz)
BFS | YT | 88.6% | 12 | 3.25 | 48 | 34.71% | 19.19% | 200 | 200
 | PK |  |  |  |  |  |  |  | 
 | WK |  |  |  |  |  |  |  | 
 | LJ | 77.4% | 8.1 | 4.77 | 32(enhanced) | 23.87% | 12.79% | 150 | 300
PageRank | YT | 93.4% | 11.02 | 4.53 | 22(enhanced) | 28.42% | 25.45% |  | 
 | PK | 90.5% | 12.02 | 3.01 | 24(enhanced) | 31.02% | 27.76% |  | 
 | WK | 86.5% | 8.01 | 6.5 | 16(enhanced) | 31.02% | 27.67% |  | 
 | LJ | 93.4% | 11.02 | 4.53 | 22(enhanced) | 28.42% | 25.45% |  | 
Resource utilization

## Slide 20: Evaluation on VCU110 (Cont’d)
Performance
Algorithm | Graph | Runtimes (seconds) | Speedup over ForeGraph | α (overlapping factor)
BFS | YT | 0.0032 | 3.1x | 1.0
 | PK | 0.0253 | - | 1.0
 | WK | 0.0154 | 1.2x | 1.8
 | LJ | 0.168 | 2.7x | 1.0
PageRank | YT | 0.0116 | 2.5x | 1.28
 | PK | 0.0971 | - | 1.0
 | WK | 0.0515 | 1.0x | 2.41
 | LJ | 0.276 | 2.1x | 1.0

## Slide 21: Evaluation on VCU110 (Cont’d)
Reduction on DRAM/FPGA data transmission amount

## Slide 22: Evaluation on VCU118
Resource utilization
 | BFS | PageRank
#pipelines | 32(enhanced) | 18(enhanced)
LUT | 22.85% | 12.72%
FF | 15.48% | 14.10%
BRAM | 85.92% | 95.0%
URAM | 11.88% | 59.38%
Fpipe (MHZ) | 150 | 150
Fbram (MHz) | 300 | 300
Performance
Algorithm | Graph | Runtime (seconds) | Speedups over ForeGraph | α | Speedup over VCU110
BFS | YT | 0.0032 | 3.1x | 1.0 | 1.0x
 | PK | 0.0253 | - | 1.0 | 1.0x
 | WK | 0.0205 | 1.1x | 2.41 | 0.66x
 | LJ | 0.168 | 2.7x | 1.0 | 1.0x
PageRank | YT | 0.0101 | 3.0x | 1.064 | 1.2x
 | PK | 0.0972 | - | 1.0 | 1.0x
 | WK | 0.0434 | 1.2x | 2.71 | 1.2x
 | LJ | 0.219 | 2.6x | 1.0 | 1.3x

## Slide 23: Outline
Background and Motivation
Our Solution: FabGraph
Tech. details
Evaluation
Conclusion and Future Work

## Slide 24: Conclusion
Two-level vertex caching mechanism is effective in improving the performance of graph processing on FPGA-DRAM platforms
Two-level vertex caching mechanism can even help FPGA boards configured with small BRAM but large URAM to achieve better performance than expensive FPGA boards with large BRAM

## Slide 25: Future works
Performance Scaling
  Vertical scaling – FPGA-HBM2 platform
  Better horizontal scaling

## Slide 26: Thanks!