## Slide 1: ParaDRo: A Parallel Deterministic Router Based on Spatial Partitioning and Scheduling
Chin Hau Hoo, Akash Kumar
Notes: There are two parts to the title, I will explain each individually

## Slide 2: Moore’s law driving FPGA advancement
Xilinx XC2064
64 LUTs
Xilinx Zynq Ultrascale+
500,000+ LUTs
Notes: This first FPGA has X number of LUTs
So what is an f

## Slide 3: What is the problem?
Notes: In other words, the capacity of fpga is growing faster than the ability of design tools to effectively utilize it

## Slide 4: Why?
End of Dennard’s scaling
Increasing the clock speed of processor is no longer a viable solution to reduce execution time
“Power wall”

## Slide 5: FPGA design flow
Logic synthesis
Technology mapping
Packing
Placement
Routing
Bitstream generation
HDL
Percentage of execution time in various stages
Notes: To better understand the design productivity gap, let’s look at a typical fpga design flow. Therefore, in this talk we are focusing on routing.
Data is obtained using the 8 benchmarks in slide 29

## Slide 6: Pathfinder
CLB
CLB
CLB
CLB
Output pin
Input pin
Congested?
No
Yes
No
Yes
Has nets to route?
Initialize
Rip up net
Route net
Done
Update history congestion costs
Update present congestion costs
Notes: So what is the algorithm to perform routing in fpgas? Pathfinder
The figure on the left shows an example arch of fpga
Pathfinder builds a graph to model the the routing resources in this fpga during initialization

## Slide 7: Pathfinder
CLB
CLB
CLB
CLB
Output pin
Input pin
Congested?
No
Yes
No
Yes
Has nets to route?
Initialize
Rip up net
Route net
Done
Update history congestion costs
Update present congestion costs

## Slide 8: Pathfinder
CLB
CLB
CLB
CLB
Output pin
Input pin
Congested?
No
Yes
No
Yes
Has nets to route?
Initialize
Rip up net
Route net
Done
Update history congestion costs
Update present congestion costs

## Slide 9: Pathfinder
CLB
CLB
CLB
CLB
Output pin
Input pin
Congested?
No
Yes
No
Yes
Has nets to route?
Initialize
Rip up net
Route net
Done
Update history congestion costs
Update present congestion costs

## Slide 10: Pathfinder
CLB
CLB
CLB
CLB
Output pin
Input pin
Congested?
No
Yes
No
Yes
Has nets to route?
Initialize
Rip up net
Route net
Done
Update history congestion costs
Update present congestion costs
Notes: Path finder is similar to Dijktra’s algorithm except that the cost is updated dynamically

## Slide 11: Pathfinder
CLB
CLB
CLB
CLB
Output pin
Input pin
Net 2 source
Net 1 source
Net 1 sink
Net 2 sink
Congested?
No
Yes
No
Yes
Has nets to route?
Initialize
Rip up net
Route net
Done
Update history congestion costs
Update present congestion costs

## Slide 12: Pathfinder
CLB
CLB
CLB
CLB
Output pin
Input pin
Net 2 source
Net 1 source
Net 1 sink
Net 2 sink
Congested?
No
Yes
No
Yes
Has nets to route?
Initialize
Rip up net
Route net
Done
Update history congestion costs
Update present congestion costs

## Slide 13: Pathfinder
CLB
CLB
CLB
CLB
Output pin
Input pin
Net 2 source
Net 1 source
Net 1 sink
Net 2 sink
Congested?
No
Yes
No
Yes
Has nets to route?
Initialize
Rip up net
Route net
Done
Update history congestion costs
Update present congestion costs

## Slide 14: Observations
Pathfinder is largely sequential
Route of a net depends on the routes taken by nets routed before it
Is it possible to create a scalable and deterministic parallel FPGA router?
Notes: No free lunch
  Complex trade off between speedup, quality of result, and determinism

## Slide 15: Existing deterministic routers
 | Platform | Method | Speedup
Gort, 2010 (Coarse) | Shared memory | Net partitioning | Moderate
Gort, 2010 (Fine) | Shared memory | Parallel maze expansion | Low
Gort, 2010 (Hybrid) | Shared + Distributed memory | Net partitioning + Parallel maze expansion | Moderate
Gort, 2012 | Distributed memory | Net partitioning | Moderate
Gort, 2012 (Enhanced) | Distributed memory | Net partitioning + Conditional net rerouting | High
Shen, 2015 | Distributed memory | Net partitioning | Moderate
Shen, 2017 | GPU | Net partitioning + Parallel maze expansion | Very high
ParaDRo | Shared memory | Net partitioning + Scheduling | High
Notes: Net partitioning is used in almost all approaches to ensure determinism

## Slide 16: Algorithm overview
Initialization
  Recursive bi-partitioning
    Pre-processing
    Finding the optimal cut-line
  Multi-sink net decomposition and virtual net generation
  Overlap graph coloring and task graph generation
Routing virtual nets in the task graph associated with each node in the bi-partitioning tree

## Slide 17: Recursive bi-partitioning
0
1
2
3
4
5
6
7
8
FPGA Columns
A
start=0, end=3
B
start=0, end=2
F
start=5, end=8
E
start=5, end=7
D
start=4, end=6
C
start=3, end=5
P0
Nets: C, D
P1
Nets: A, B
P2
Nets: E, F

## Slide 18: Recursive bi-partitioning – Pre-processing
0
1
2
3
4
5
6
7
8
A
B
0
1
2
3
4
5
6
7
8
FPGA Columns
A
start=0, end=3
B
start=0, end=2
F
start=5, end=8
E
start=5, end=7
D
start=4, end=6
C
start=3, end=5
nets_start
C
D
E
F

## Slide 19
0
1
2
3
4
5
6
7
8
B
A
start=0, end=3
B
start=0, end=2
F
start=5, end=8
E
start=5, end=7
D
start=4, end=6
C
start=3, end=5
nets_end
A
D
C
E
F
0
1
2
3
4
5
6
7
8
FPGA Columns
Recursive bi-partitioning
– Pre-processing

## Slide 20: Recursive bi-partitioning – Pre-processing
A
start=0, end=3
B
start=0, end=2
F
start=5, end=8
E
start=5, end=7
total_workload_after
3
0
0
0
0
0
0
0
0
3
0
0
2
0
0
0
0
0
3
0
0
2
1
0
0
0
0
3
0
0
2
1
1
0
0
0
3
0
0
2
1
3
0
0
0
0
0
0
0
0
0
0
0
0
0
1
2
3
4
5
6
7
8
2
0
0
0
0
0
0
0
0
9
6
6
6
4
3
0
0
0
Prefix sum from the last element
D
start=4, end=6
C
start=3, end=5
0
1
2
3
4
5
6
7
8
FPGA Columns

## Slide 21: Recursive bi-partitioning – Pre-processing
total_workload_before
0
0
1
2
0
0
0
0
0
0
0
1
2
0
2
0
0
0
0
0
1
2
0
2
1
0
0
0
0
1
2
0
2
1
1
0
0
0
1
2
0
2
1
1
2
0
0
0
0
0
0
0
0
0
0
1
2
3
4
5
6
7
8
0
0
0
2
0
0
0
0
0
0
0
1
3
3
5
6
7
9
Prefix sum from the first element
A
start=0, end=3
B
start=0, end=2
F
start=5, end=8
E
start=5, end=7
D
start=4, end=6
C
start=3, end=5
0
1
2
3
4
5
6
7
8
FPGA Columns

## Slide 22: Recursive bi-partitioning - Finding the optimal cut-line
total_workload_before
9
6
6
6
4
3
0
0
0
0
1
2
3
4
5
6
7
8
0
0
1
3
3
5
6
7
9
0
1
2
3
4
5
6
7
8
total_workload_after
9
6
6
5
1
0
5
6
7
0
1
2
3
4
5
6
7
8
9
9
Absolute workload diff
Min diff
Min diff
Min diff
Min diff
Min diff
Cutline
0
1
2
3
4
5
6
7
8
nets_start
A
B
C
D
E
F
0
1
2
3
4
5
6
7
8
D
B
A
C
E
F
nets_end
P0
Nets: C, D
P1
Nets: A, B
P2
Nets: E, F

## Slide 23: Problem when routing
P0
Nets: C, D
P1
Nets: A, B
P2
Nets: E, F
Thread 0
Thread 1
C
D
A
B
E
F
Idle
Net C and D are overlapping!

## Slide 24: Multi-sink net decomposition and virtual net generation
C
D
C1
D
C2
OR
D1
C1
C2
D1
C1
C2
Less overlap between virtual nets
Notes: When we break

## Slide 25: Overlap graph coloring and task graph generation
D1
C1
C2
C1
C2
D1
C1
C2
D1
C1
C2
D1
Graph coloring to identify parallelism
Conversion to directed task graph to minimize idle time
Overlap graph
Notes: Graph coloring to identify parallelism

## Slide 26: Overlap graph coloring and task graph generation
D1
C1
C2
Graph coloring to identify parallelism
Conversion to directed task graph to minimize idle time
Overlap graph
C3
C1
C2
D1
C3
C1
C2
D1
C3
C1
C2
D1
C3
Notes: Graph coloring to identify parallelism

## Slide 27: Routing the nets with scheduling
Thread 0
Thread 1
Without scheduling
With scheduling
VS
Thread 0
Thread 1
C
D
A
B
E
F
Idle
C2
D
A
B
E
F
P0
Nets: C1, C2, C3, D
P1
Nets: A, B
P2
Nets: E, F
C1
C3

## Slide 28: Ensuring convergence
When the number of congested nets drops below a predefined threshold, ParaDro only reroutes congested nets
When rerouting only congested nets, the bounding boxes of virtual nets are expanded back to their original size
C1
D
C2
D
C1
C2

## Slide 29: Experimental Setup
Dual Intel® Xeon® E5-2680 v3 + 128 GB RAM
RHEL 6.8 + Linux kernel 2.6.32
gcc 7 with -O3 flag
Benchmark | Total nets | Minimum channel width
stereovision1 | 10,797 | 104
LU8PEEng | 15,990 | 114
stereovision2 | 34,501 | 154
LU32PEEng | 53,199 | 174
neuron | 54,056 | 206
stereo_vision | 61,883 | 228
segmentation | 125,592 | 292
denoise | 257,425 | 310

## Slide 30: Speedup of different ParaDRo variants
Chart: Speedup
| 1 thread | 2 threads | 4 threads | 8 threads | 1 thread | 2 threads | 4 threads | 8 threads | 120% min chan width | 140% min chan width
seq normal | 1 | 1.4205 | 1.6845 | 1.8504 | 1 | 1.6345 | 2.0446 | 2.4043
seq extra | 1 | 1.5888 | 1.8229 | 2.0037 | 1 | 1.7555 | 2.2507 | 2.6329
par normal | 1 | 1.766 | 2.7288 | 2.9052 | 1 | 2.0466 | 3.7063 | 4.5527
par extra | 1 | 1.6835 | 2.8665 | 3.1979 | 1 | 2.0049 | 3.8752 | 5.0563
Par: parallelism within a node as well
Extra: bipartition each internal node once more in orthogonal direction
Notes: Seq – no parallelism within the partition node
Par – parallelize the nodes within the partition e.g. C and D
Extra – orthogonal cuts in all the nodes, except the last level of the tree. Since the number of leaves is the same as the number of threads.

## Slide 31: Critical path delay
Chart: Critical path delay normalized to VTR
| stereovision1 | LU8PEEng | stereovision2 | LU32PEEng | neuron | stereo_vision | segmentation | denoise | stereovision1 | LU8PEEng | stereovision2 | LU32PEEng | neuron | stereo_vision | segmentation | denoise | 120% min chan width | 140% min chan width
1 thread | 1.0002 | 1.0023 | 1 | 1 | 1 | 0.9997 | 0.99495 | 0.99269 | 1.0006 | 1.0005 | 1.0002 | 1 | 1.0232 | 0.87226 | 0.99352 | 0.99402
2 threads | 1 | 1.0082 | 0.9924 | 1.0063 | 1 | 0.86257 | 1.0373 | 1.0428 | 1.0244 | 1.0172 | 1.0152 | 1.0163 | 1.0234 | 0.89678 | 1.0466 | 1.0479
4 threads | 1 | 1.0089 | 0.9924 | 1.0054 | 1 | 0.87685 | 1.041 | 1.0445 | 1.0248 | 1.0173 | 1.0152 | 1.0129 | 1.0016 | 0.90839 | 1.0423 | 1.0513
8 threads | 1.0002 | 1.0072 | 1.0075 | 1.0068 | 1 | 0.88102 | 1.0379 | 1.046 | 1.0248 | 1.0183 | 1.0152 | 1.0129 | 1.0016 | 0.88471 | 1.0417 | 1.0512

## Slide 32: Impact on total wirelength
Chart: Total wirelength normalized to VTR
| stereovision1 | LU8PEEng | stereovision2 | LU32PEEng | neuron | stereo_vision | segmentation | denoise | stereovision1 | LU8PEEng | stereovision2 | LU32PEEng | neuron | stereo_vision | segmentation | denoise | 120% min chan width | 140% min chan width
1 thread | 0.98724 | 1.0003 | 1.0028 | 1.0232 | 1.0064 | 1.0085 | 1.0509 | 1.0451 | 1.0245 | 1.027 | 1.013 | 1.0248 | 1.0045 | 0.99911 | 1.0502 | 1.0503
2 threads | 1.0496 | 1.1215 | 1.069 | 1.1301 | 1.0195 | 1.0217 | 1.1076 | 1.1009 | 1.0698 | 1.1299 | 1.0539 | 1.101 | 1.0106 | 1.0065 | 1.0917 | 1.0919
4 threads | 1.0497 | 1.1199 | 1.0691 | 1.1272 | 1.0186 | 1.0216 | 1.1069 | 1.0975 | 1.0721 | 1.125 | 1.055 | 1.1005 | 1.0104 | 1.0052 | 1.0863 | 1.0911
8 threads | 1.0484 | 1.1136 | 1.0691 | 1.1249 | 1.0189 | 1.0211 | 1.1072 | 1.1019 | 1.072 | 1.1214 | 1.0538 | 1.0962 | 1.0093 | 1.005 | 1.084 | 1.0865
Notes: Two factors – Restrictive bounding box and our ParaDRo partitioning

## Slide 33: Impact of enforcing sequential equivalence on speedup
Chart: Speedup
| stereovision1 | LU8PEEng | stereovision2 | LU32PEEng | neuron | stereo_vision | segmentation | denoise
non seq equi 1 thread | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
seq equi 1 thread | 0.88482 | 1.5266 | 1.3353 | 1.7621 | 1.0604 | 0.9626 | 1.0469 | 1.045
non seq equi 2 threads | 1.4991 | 2.4452 | 2.6124 | 3.6594 | 1.3918 | 1.3383 | 1.6241 | 1.4689
seq equi 2 threads | 1.4344 | 2.5509 | 2.9662 | 3.5883 | 1.919 | 1.6388 | 1.7418 | 1.9677
non seq equi 4 threads | 2.0539 | 3.8361 | 4.8662 | 8.5726 | 2.2919 | 2.3441 | 3.2276 | 3.8092
seq equi 4 threads | 2.1271 | 3.8575 | 4.4705 | 9.3703 | 2.6951 | 2.1847 | 3.5116 | 3.8438
non seq equi 8 threads | 2.3609 | 4.3418 | 5.9305 | 13.0508 | 2.8604 | 2.4147 | 4.0893 | 5.4017
seq equi 8 threads | 2.3609 | 4.3418 | 5.9305 | 13.0508 | 2.8604 | 2.4147 | 4.0893 | 5.4017

## Slide 34: Speedup comparison with existing deterministic works
Chart: Speedup
| VTR | Gort 2012 (30%) | Gort 2012 enhanced (30%) | Shen 2015 (40%) | Shen 2017 (30%) | 20% | 40% |  | Existing deterministic parallel routers | ParaDRo
1 thread | 1
2 threads | 1.53 | 5.02 | 1.56 | 1.8876 | 2.3697
4 threads | 2.2 | 7.71 | 3.15 | 3.0658 | 4.3736
8 threads | 2.8 | 9.42 | 4.62 | 3.3775 | 5.4047
GPU | 18.72
18.7
(par extra)
Notes: Gort Enhanced – only in first iteration it routes all nets.. From the second iteration only congested routes are routed.
Largest benchmark was Stereo-vision with 40K LUTs, may give convergence issues with larger benchmarks
Shen uses Bellman-Ford, easier to parallelize than Dijkstra but it is not work-optimal

## Slide 35: Impact of ‘Determinism’
Chart: Speedup
| 20% | 40% | 20% | 40% | 20% | 30% | 40% | ParaDRo | ParaFRo | ParaDiMe
2 threads | 1.8876 | 2.3697 | 10.3207 | 11.045 | 3.3114 | 3.6187 | 3.5866
4 threads | 3.0658 | 4.3736 | 15.8592 | 17.9776 | 5.8221 | 6.6839 | 6.3761
8 threads | 3.3775 | 5.4047 | 26.2455 | 27.589 | 9.2345 | 11.4042 | 10.4506
16 threads | 13.741 | 15.9617 | 15.0065
32 threads | 15.7415 | 19.754 | 18.1101
Notes: ParaFRo: FPL 2016
ParaDiMe: FCCM 2017

## Slide 36: Conclusions
Presented a deterministic parallel router - ParaDRo
Uses recursive bi-partitioning to group the nets into nodes that can be routed in parallel
Graph coloring and task scheduling are employed within the node to exploit further parallelism
Determinism affects speed-up significantly

## Slide 37
Thank you!

## Slide 38: Where are FPGAs used?
Aerospace
Prototyping
Automotive
Broadcast
Consumer Electronics
Data Center
HPC
Industrial
Medical
Test & Measurement
Wired Comms
Wireless Comms
Notes: So where are fpp

## Slide 39: Design tools
Aerospace
Prototyping
Automotive
Broadcast
Consumer Electronics
Data Center
HPC
Industrial
Medical
Test & Measurement
Wired Comms
Wireless Comms
Implement applications on FPGAs
Evaluate new FPGA architectures
Verilog-to-Routing (VTR)
Notes: Design tools is the bridge between fpga and their applications