## Slide 1: A Full-System VM-HDL Co-Simulation Framework for Servers with PCIe-Connected FPGAs
Shenghsun Cho, Mrunal Patel, Han Chen,
Michael Ferdman, Peter Milder

## Slide 2: FPGAs in Cloud Creates Debug Challenges
FPGA
FPGAs now run rapid changing server workloads
  Involve HW, SW, and OS at the same time
  Directly interact with real-world network
Impossible to debug with testbenches
Forces developers to debug on the target systems
PCIe
Network

## Slide 3: Debugging on Target Systems is Difficult
Long debug iteration time
  Time-consuming FPGA synthesis and P&R
Poor visibility for identifying bugs
  Limited hardware probes
  OS hang and reboot without useful information

## Slide 4: Our VM-HDL Co-Simulation Framework
Run the same HW, SW, and OS as the target systems
Provides network capability for HDL simulation
Reduces debug iteration time
Provides full visibility
Co-Simulation
VM
HDL
Target System

## Slide 5: Outline
Overview
FPGA Debugging Challenges
Our VM-HDL Co-Simulation Framework
Case Studies
Conclusions

## Slide 6: Long Debug Iteration Time
Synthesis, place and route can take many hours
Not much help from multi cores/machines
Timing violations force re-running the whole process

## Slide 7: Poor Visibility for Debugging
Very limited FPGA probes and waveform buffer
Requires FPGA P&R to add or change probes
OS reboots without providing enough information

## Slide 8: State Of The Art
Systems are too complex for testbenches
HW-SW Co-Sim cannot handle OS and network
Existing full-system simulation is targeting SoC ASICs
  Used in early stage evaluation with high-level models

## Slide 9: Outline
Overview
FPGA Debugging Challenges
Our VM-HDL Co-Simulation Framework
Case Studies
Conclusions

## Slide 10: Our VM-HDL Co-Simulation Framework

## Slide 11: Our VM-HDL Co-Simulation Framework
HDL Simulator
Virtual Machine
Emulated Hardware
FPGA
Host
Software
PCIe Block
Operating System
Host Hardware
Hardware Design
PCIe Link
FPGA PCIe
Simulation Bridge
Inter-Process Queue
FPGA
Pseudo Device
Unchanged
Components
Co-Sim
Components

## Slide 12: Our VM-HDL Co-Simulation Framework
HDL Simulator
Virtual Machine
Emulated Hardware
Software
PCIe Block
Operating System
Host Hardware
Hardware Design
PCIe Link
FPGA PCIe
Simulation Bridge
Inter-Process Queue
FPGA
Pseudo Device
Attach GDB
Save Waveform
Full visibility and no modification to HW, SW, and OS

## Slide 13: Network Support
HDL Simulator
Virtual Machine
Emulated Hardware
HDL Simulator
Virtual Machine
Software
Operating System
Emulated Hardware
Hardware Design
PCIe Link
FPGA PCIe Simulation Bridge
FPGA
Pseudo Device
FPGA NIC
Simulation Bridge
NIC Queue
PCIe Queue
NIC Tap

## Slide 14: Network Support
HDL Simulator
Virtual Machine
Emulated Hardware
HDL Simulator
Virtual Machine
Software
Operating System
Emulated Hardware
Hardware Design
PCIe Link
FPGA PCIe Simulation Bridge
FPGA
Pseudo Device
FPGA NIC
Simulation Bridge
NIC Queue
PCIe Queue
NIC Tap
Inbound
Packets

## Slide 15: Network Support
HDL Simulator
Virtual Machine
Emulated Hardware
HDL Simulator
Virtual Machine
Software
Operating System
Emulated Hardware
Hardware Design
PCIe Link
FPGA PCIe Simulation Bridge
FPGA
Pseudo Device
FPGA NIC
Simulation Bridge
NIC Queue
PCIe Queue
NIC Tap
Outbound
Packets

## Slide 16: Outline
Overview
FPGA Debugging Challenges
The VM-HDL Co-Simulation Framework
Case Studies
Conclusions

## Slide 17: Evaluation Setup
Target system
  Dual-Socket Xeon server with Xilinx Virtex 7 XC7V690 FPGA
Co-Simulation
  QEMU VM with KVM support
  VCS HDL simulator
  ZeroMQ inter-process communication library
OS and software
  Ubuntu 16.04 with Kernel 4.4.0
  Software and driver to utilize FPGA designs

## Slide 18: Case Study: Sorting Offload
Compare iteration time of a target system and Co-Sim
11% FPGA LUT utilization after place and route
FPGA
PCIe Block
Hardware Design
Sorting Engine
DMA
result
input
Host
Software
Operating System
Device Driver
Host Hardware
PCIe

## Slide 19: Debug Iteration Time Comparison
 | Target System (minutes:seconds) | Co-Simulation (minutes:seconds)
Compilation | - | 1m:10s
Synthesis | 18m:03s | -
Place and Route | 35m:40s | -
Reboot | 2m:33s | 0m:25s
Execution | ≈0m:00s | 0m:03s
Total | 56m:16s | 1m:38s

## Slide 20: Hardware Probe Change Comparison
Hardware | First Time | Add Probes | Change Probes
Synthesis | 17m:48s | - | -
P&R | 39m:16s | 42m:22s | 58m:52s
Reboot | 1m:26s | 1m:26s | 1m:26s
Execution | ≈0m:00s | ≈0m:00s | ≈0m:00s
Total | 58m:30s | 43m:48s | 60m:18s
(unit: minutes:seconds)
Co-Simulation |  |  | 
Simulation | 1m:33s |  | 
Total | 1m:33s | 0m:00s | 0m:00s

## Slide 21: Case Study: Network Interface Card
Confirm the functionality of the NIC bridge in Co-Sim
  Co-Sim sustains 15KB/sec connections to public network
FPGA
PCIe Block
Hardware Design
DMA
Inbound Packet
Outbound Packet
Host
Software
Operating System
Device Driver
Host Hardware
PCIe
Ethernet Block

## Slide 22: Conclusions
Debugging FPGAs in datacenters is difficult
  Long debug iteration time
  Poor visibility
Our VM-HDL Co-Sim framework solves these problems
  Same HW, SW, and OS in simulation and target systems
  Provides network capability to HDL simulation
  Significantly reduces the debug iteration time
  Full visibility for identifying bugs
Source/Demo can be downloaded at:
http://compas.cs.stonybrook.edu/projects/fpgacloud/vm-hdl-cosim/