## Slide 1: A Framework for Generating High Throughput CNN Implementations on FPGAs
Hanqing Zeng, Ren Chen, Chi Zhang and Viktor Prasanna
University of Southern California
fpga.usc.edu
Feb. 26, 2018
FPGA 18, Monterey, CA

## Slide 2: Outline
Background & overview
Algorithmic optimizations
Hardware mapping methodology
Automatic design generation
Experimental results
Conclusion

## Slide 3: Convolutional Neural Networks
Latency driven workloads
Throughput driven workloads
Autonomous driving
Natural language processing
Security & Surveillance
Medical imaging diagnosis
Notes: CNNs have been applied to many applications.
In some cases, for example, autonomous driving and NLP, you really expect the CNN to have real-time response. So these are latency driven workload.
In other cases, for example, CNNs are used to analyze huge volume of videos or images for security and medical diagnosis, then throughput is the key metric.
In this work, we focus on throughput optimization.

## Slide 4: Framework Overview
Algorithmic Optimization
Hardware Mapping
CNN model parameters
Input
Output
Shape of 2D images
Data layout
Target FPGA specification
Throughput-optimized accelerator
Suggestions for optimizing next generation DL chips
Auto Design Generation
Notes: First of all, the framework has an algo module. It takes as input CNN model params and shape of 2D input images, and generates a data layout which can be very efficiently processed by hardware accelerators.
Then the Hardware mapping module needs to know about the spec of the target FPGA, in order to generate the throughput optimized accelerator. Notice that hardware mapping does not depend on the CNN parameters. In fact, the mapping module will provide feedback to the algorithmic optimization modules so that the data layout can best fit the FPGA.
Lastly, the mapping module from the high level can provide suggestions for designing next generation DL chips.

## Slide 5
Target FPGA
VGG16
AlexNet
FCN-16s
...
Various CNN Models
Segmentation
Classification
Various image sizes
...
Corresponding data layout
...
Framework
Accelerator design
Generic high throughput accelerator
No need to reconfigure for a specific CNN
Notes: Let’s see a more concrete example.
Suppose we want to use a fixed FPGA to accel many different kinds of CNNs. The framework synthesize an accelerator design onto the device.
After that, the application specific CNNs come into picture. These can be drastically different networks. The input image data also come. They can be small images, or large images.
However, the hardware is already configured. Then how do we optimize a specific workload? The framework will adjust the data layout to be fed to hardware so that high throughput can always be sustained.
In summary, the accelerator is generic.

## Slide 6: Challenges in Designing a Generic Accelerator
Computation complexity
Variation in CNN model parameters
Variation in input image sizes
Kernel filters
Input
Output
Kernel filters
Input
Output
Kernel filters
Input
Output
Input channels
Output channels
Image size
Kernel window size
AlexNet:
VGG16:
FCN-16s:
Notes: 3.5 min

## Slide 7: Outline
Background & overview
Algorithmic optimizations
Hardware mapping methodology
Automatic code generation
Experimental results
Conclusion

## Slide 8: Frequency Domain Convolution with Overlap-and-Add
FFT of inputs:
FFT of kernels:
Hadamard product:
IFFT of outputs:
Notes: Our framework is based on frequency domain convolution. Let’s first review how to perform frequency domain convolution with a known technique called overlap-and-add.
The motivation of overlap-add is that we want to use a fixed size FFT architecture in hardware to handle images of various sizes. How do we do it?
We first partition the images based on the FFT size. Then we do some paddings and send the images to frequency domain, by Fourier transform. As an example, suppose we have 256 input channels, and our FFT size is 16 point, then the number of operations required here is 0.3 million.
Of course, we also need to send the kernel filters to frequency domain. Notice that we don’t need to perform any operations in this step, since kernels are fixed during inferencing, and we can pre-store the frequency domain representation of kernel filters.
Next step is that we take kernels and images and perform hadamard product on them. Hadamard product is basically elementwise multiplication. we require 17 M operations in our example.
Finally, we take the matrices back to time domain, and combine the partitions into a complete image. When combining the images, the partitions need certain amounts of overlap. That’s why we call this technique Overlap-and-Add.

## Slide 9: Limitation of Overlap-and-Add (OaA)
☑ Computation complexity
☑ Variation in kernel window size
✘ Variation in image sizes
✘ Flexibility in hardware design
e
Wasted computation on padding!
Algorithm | # operations
Space domain conv. | 
Freq. domain (OaA) | 
Algorithm | # operations
Space domain conv. | 
Freq. domain (OaA) | 
Computation complexity for input images
Space Conv.
Notes: This known technique seems very good.
Because of frequency domain convolution, we save a lot of computation compared with space domain convolution. And OaA can be applied to kernels of various sizes as long as the FFT size is larger than the kernel size.
But OaA is not very robust when dealing with images of various sizes.
For example, here we have a l

## Slide 10: Optimization 1: Concatenate-and-Pad
☑ Variation in image sizes
☑ Flexibility in hardware design
e
e
e
e
e
e
e
e
e
Reducing wasted computation of OaA

## Slide 11: Computation Complexity of CaP
Given a FFT size , kernel window size , CaP guarantees its computation complexity (number of operations) to be less than times the optimal.
30%
14%

## Slide 12: Optimization 2: Freq. Domain Loop Tiling
Data reuse scheme in batch inferencing
  Kernel oriented
Loop tiling on kernels
  Partition the input/output channels
  Kernel tiles fits on-chip memory
☑ Variation in number of input channels
☑ Variation in number of output channels

## Slide 13: Summary of Algorithmic Optimizations
FFT size based on hardware spec?
Overlap-and-Add
Concatenate-and-Pad
Frequency domain loop tiling
Data layout for frequency domain convolution
CNN model parameters
Shape of 2D images
Freq. domain convolution
☑ Comp. complexity
Overlap-and-Add
☑ Various kernel window sizes
Concatenate-and-Pad
☑ Various input image sizes
Freq. domain loop tiling
☑ Various input channels
☑ Various output channels

## Slide 14: Outline
Background & overview
Algorithmic optimizations
Hardware mapping methodology
Automatic design generation
Experimental results
Conclusion

## Slide 15: Hardware Mapping Overview
CNN model
Shape of 2D images
Data layout
FPGA spec.
Throughput-optimized accelerator
Suggestion to next generation DL chips
Algorithmic Optimization
Hardware Mapping
Auto Design Generation
Optimal generic accelerator:
Communication capacity?
Computation capacity?
Define optimal data layout:
Partition images (FFT size)?
Partition kernels (tiling size)?
Suggestions for optimizing next gen DL chip:
How much DSP?
How large on-chip buffer?
How fast external BW?

## Slide 16: Accelerator Architecture
…
…
SPN
1D
1D
1D
1D
…
…
Parallel-Serial
…
…
SPN
1D
1D
1D
1D
2D FFT
2D IFFT
MAC array
From external memory
To external memory
 | Communication |  | Computation | 
 | External mem traffic | On-chip data reuse | Complexity | DSP consumption
FFT size ↑ | ↑ | ↓ | ↓ | ↓
FFT size ↓ | ↓ | ↑ | ↑ | ↑

## Slide 17: Device Coefficient
Categorize the target FPGA by
  DSP resources
  On-chip memory size
  External memory bandwidth
High level abstraction
Device coefficient
  Balance communication & computation
DRAM
FPGA
Notes: For CNN workloads

## Slide 18: Performance Analysis
FFT Size
Throughput (Normalized)
FFT Size
Throughput (Normalized)
-point FFT
-point FFT
Communication bound
Computation bound

## Slide 19: Design Space Exploration
FFT Size
Throughput (Normalized)
FFT Size
Throughput (Normalized)
FFT Size
Throughput (Normalized)
Stratix-V:
Next generation of Deep Learning chips:
…

## Slide 20: Outline
Background & overview
Algorithmic optimizations
Hardware mapping methodology
Automatic design generation
Experimental results
Conclusion

## Slide 21: Automatic Design Generation
Time to generate a complete design:

## Slide 22: Outline
Background & overview
Algorithmic optimizations
Hardware mapping methodology
Automatic design generation
Experimental results
Conclusion

## Slide 23: Reduction in Computation Complexity
2.3x
3.7x
AlexNet
FCN-16s
VGG16

## Slide 24: Use of Device Coefficient
Optimal design point for Stratix-V:
FFT of point
Tiling size of

## Slide 25: Comparison with State-of-the-Art
 | FPL 16 | FPL 16 | FPGA 17 | Our work
FPGA | Virtex-7 VC709 | Stratix-V GXA7 | Stratix-V GXA7 | Stratix-V GXA7
Frequency (MHz) | 156 | 100 | 200 | 200
Precision | 16b fixed | 8-16b fixed | 32b float | 16b fixed
DSP | 2144 (60%) | 256 (100%) | 224 (88%) | 256 (100%)
On-chip RAM | 956 (65%) | 1152 (61%) | 1208 (64%) | 1377 (73%)
Throughput (GOPS) | 565.9 | 134.1 | 83.0 | 780.6
AlexNet Results
5.8x

## Slide 26: Comparison with State-of-the-Art
 | FPGA 16 | FPGA 17 | FPGA 17 | FPGA 17 | Our work
FPGA | Zynq XC7Z045 | Arria-10 GX1150 | Arria-10 GX1150 | Stratix-V GXA7 | Stratix-V GXA7
Frequency (MHz) | 150 | 150 | 385 | 200 | 200
Precision | 16b fixed | 8-16b fixed | 8-16b fixed | 32b float | 16b fixed
DSP | 780 (89%) | 1518 (100%) | 1378 (91%) | 224 (88%) | 256 (100%)
On-chip RAM | 486 (87%) | 1900 (70%) | 1450 (53%) | 1208 (64%) | 1377 (73%)
Throughput (GOPS) | 137.0 | 645.3 | 1790 | 123.5 | 669.1
VGG16 Results
4.9x
550 GOPS (First work to accelerate FCN)
FCN Results

## Slide 27: Conclusion
Algorithmic optimizations
  Concatenate-and-Pad: Computation complexity reduction
  CaP + OaA + Tiling: Leading to a generic accelerator design
Hardware mapping methodology
  Device coefficient: Simple and precise design space exploration
  Device coefficient: Optimizing of next generation DL chips
Performance improvements in throughput
  AlexNet: 5.8x; VGG16: 4.9x

## Slide 28
Thank You!
fpga.usc.edu