## Slide 1: Dynamically Scheduled High-level Synthesis
Lana Josipović, Radhika Ghosal, Paolo Ienne
École Polytechnique Fédérale de Lausanne (EPFL)
February 2018

## Slide 2: High-level Synthesis and Static Scheduling
High-level synthesis (HLS) is the future of reconfigurable computing
  Design circuits from high-level programming languages
Classic HLS relies on static schedules
  Each operation executes at a cycle fixed at synthesis time
Scheduling dictated by compile-time information
  Maximum parallelism in regular applications
  Limited parallelism when information unavailable at compile time (i.e., latency, memory or control dependencies)

## Slide 3: The Limitations of Static Scheduling
1: x[0]=5 → ld hist[5]; st hist[5];
2: x[1]=4 → ld hist[4]; st hist[4];
3: x[2]=4 → ld hist[4]; st hist[4];
for (i=0; i<N; i++) {
hist[x[i]] = hist[x[i]] + weight[i];
}

## Slide 4: The Limitations of Static Scheduling
for (i=0; i<N; i++) {
hist[x[i]] = hist[x[i]] + weight[i];
}
1: x[0]=5 → ld hist[5]; st hist[5];
2: x[1]=4 → ld hist[4]; st hist[4];
3: x[2]=4 → ld hist[4]; st hist[4];
RAW

## Slide 5: The Limitations of Static Scheduling
Static scheduling (any HLS tool)
  Inferior when memory accesses cannot be disambiguated at compile time
RAW
for (i=0; i<N; i++) {
hist[x[i]] = hist[x[i]] + weight[i];
}
1: x[0]=5 → ld hist[5]; st hist[5];
2: x[1]=4 → ld hist[4]; st hist[4];
3: x[2]=4 → ld hist[4]; st hist[4];

## Slide 6: The Limitations of Static Scheduling
Static scheduling (any HLS tool)
  Inferior when memory accesses cannot be disambiguated at compile time
Dynamic scheduling
  Maximum parallelism: Only serialize memory accesses on actual dependencies
for (i=0; i<N; i++) {
hist[x[i]] = hist[x[i]] + weight[i];
}
1: x[0]=5 → ld hist[5]; st hist[5];
2: x[1]=4 → ld hist[4]; st hist[4];
3: x[2]=4 → ld hist[4]; st hist[4];
RAW

## Slide 7
Towards Dynamic Scheduling
Overcoming the conservatism of statically scheduled HLS
  Dynamically selecting the schedule at runtime1
  Application-specific dynamic hazard detection2
  Pipelining particular classes of irregular loops3
1 Liu et al. Offline synthesis of online dependence testing: Parametric loop pipelining for HLS. FCCM ’15.
2 Dai et al. Dynamic hazard resolution for pipelining irregular loops in high-level synthesis. FPGA ‘17.
3 Tan et al. ElasticFlow: A complexity-effective approach for pipelining irregular loop nests. ICCAD ‘15.

## Slide 8
Towards Dynamic Scheduling
1 Liu et al. Offline synthesis of online dependence testing: Parametric loop pipelining for HLS. FCCM ’15.
2 Dai et al. Dynamic hazard resolution for pipelining irregular loops in high-level synthesis. FPGA ‘17.
3 Tan et al. ElasticFlow: A complexity-effective approach for pipelining irregular loop nests. ICCAD ‘15.
Overcoming the conservatism of statically scheduled HLS
  Dynamically selecting the schedule at runtime1
  Application-specific dynamic hazard detection2
  Pipelining particular classes of irregular loops3
    Some dynamic behavior, but still based on static scheduling

## Slide 9
Dynamically Scheduled Circuits
1 Budiu et al. Dataflow: A complement to superscalar. ISPASS ’05.
2 Carloni et al. Theory of latency-insensitive design. TCAD '01.
3 Cortadella et al. Synthesis of synchronous elastic architectures. DAC '06.
4 Vijayaraghavan et al. Bounded dataflow networks and latency-insensitive circuits. MEMOCODE '09.
  Efforts in the asynchronous domain 1
  Structures of asynchronous handshake components
  Each operation executes as soon as all of its inputs arrive
  Dataflow, latency-insensitive, elastic 2, 3, 4
  Synchronous methodologies for achieving dynamic scheduling

## Slide 10
Dynamically Scheduled Circuits
1 Budiu et al. Dataflow: A complement to superscalar. ISPASS ’05.
2 Carloni et al. Theory of latency-insensitive design. TCAD '01.
3 Cortadella et al. Synthesis of synchronous elastic architectures. DAC '06.
4 Vijayaraghavan et al. Bounded dataflow networks and latency-insensitive circuits. MEMOCODE '09.
    How to create dynamically scheduled circuits from high-level programs?
  Efforts in the asynchronous domain 1
  Structures of asynchronous handshake components
  Each operation executes as soon as all of its inputs arrive
  Dataflow, latency-insensitive, elastic 2, 3, 4
  Synchronous methodologies for achieving dynamic scheduling

## Slide 11
Outline
Introduction
Background: elastic circuits
Synthesizing elastic circuits
Evaluation
Conclusion

## Slide 12
Elastic Circuits1
  Every component communicates via a pair of handshake signals
Component 1
Component 2
data
1 Cortadella et al. Synthesis of synchronous elastic architectures. DAC '06.
valid
ready

## Slide 13
Buff
Elastic Components1
1 Cortadella et al. Synthesis of synchronous elastic architectures. DAC '06.
FIFO
Fork
Join
Branch
Merge
  Elastic buffer
  Elastic FIFO
  Fork
  Merge
  Join
  Branch

## Slide 14
Elastic Components1
1 Cortadella et al. Synthesis of synchronous elastic architectures. DAC '06.
Buff
FIFO
Fork
Join
Branch
Merge
  Elastic buffer
  Elastic FIFO
  Fork
  Merge
  Join
  Branch

## Slide 15
Elastic Components1
1 Cortadella et al. Synthesis of synchronous elastic architectures. DAC '06.
Fork
Buff
FIFO
Join
Branch
Merge
  Elastic buffer
  Elastic FIFO
  Fork
  Merge
  Join
  Branch

## Slide 16
Elastic Components1
1 Cortadella et al. Synthesis of synchronous elastic architectures. DAC '06.
Join
Buff
FIFO
Fork
Branch
Merge
  Elastic buffer
  Elastic FIFO
  Fork
  Merge
  Join
  Branch

## Slide 17
Elastic Components1
1 Cortadella et al. Synthesis of synchronous elastic architectures. DAC '06.
Branch
Buff
FIFO
Fork
Join
Merge
  Elastic buffer
  Elastic FIFO
  Fork
  Merge
  Join
  Branch

## Slide 18
Elastic Components1
1 Cortadella et al. Synthesis of synchronous elastic architectures. DAC '06.
Merge
Buff
FIFO
Fork
Join
Branch
  Elastic buffer
  Elastic FIFO
  Fork
  Merge
  Join
  Branch

## Slide 19
Memory subsystem
  Load ports
  Store ports
  data
  address
  data
  address
  data
  address
  data
  address
LD
LD
ST
ST
Elastic Components
+
−
>
=
  Functional units
  Memory interface

## Slide 20
Outline
Introduction
Background: elastic circuits
Synthesizing elastic circuits
Evaluation
Conclusion

## Slide 21
Synthesizing Elastic Circuits

## Slide 22
Synthesizing Elastic Circuits
Basic block
  From C to intermediate graph representation
  LLVM compiler framework
for (i=0; i<N; i++) {
hist[x[i]] = hist[x[i]] + weight[i];
}

## Slide 23
Synthesizing Elastic Circuits
i
  Constructing the datapath
  Each operator corresponds to a functional unit
LD x[i]
+
1
<
N
LD hist[x[i]]
LD weight[i]
ST hist[x[i]]
+
for (i=0; i<N; i++) {
hist[x[i]] = hist[x[i]] + weight[i];
}

## Slide 24
Synthesizing Elastic Circuits
  Merge for each variable entering the BB
  Implementing control flow
LD x[i]
Mg
+
1
Start: i=0
<
N
LD hist[x[i]]
LD weight[i]
ST hist[x[i]]
+
for (i=0; i<N; i++) {
hist[x[i]] = hist[x[i]] + weight[i];
}

## Slide 25
Synthesizing Elastic Circuits
  Branch for each variable exiting the BB
  Implementing control flow
LD x[i]
Mg
+
1
Start: i=0
Br
<
N
LD hist[x[i]]
LD weight[i]
ST hist[x[i]]
+
Exit: i=N
for (i=0; i<N; i++) {
hist[x[i]] = hist[x[i]] + weight[i];
}

## Slide 26
  Inserting Forks
Synthesizing Elastic Circuits
  Fork after every node with multiple successors
LD x[i]
Mg
Fork
+
1
Start: i=0
Fork
Br
<
N
LD hist[x[i]]
LD weight[i]
ST hist[x[i]]
+
Exit: i=N
Fork
for (i=0; i<N; i++) {
hist[x[i]] = hist[x[i]] + weight[i];
}

## Slide 27
Adding Elastic Buffers
  Elastic buffers and circuit functionality
LD hist[x]
LD weight[i]
+

## Slide 28
  Elastic buffers and circuit functionality
LD hist[x]
LD weight[i]
+
Buff
Adding Elastic Buffers

## Slide 29
  Elastic buffers and circuit functionality
LD hist[x]
LD weight[i]
+
Buff
  Buffer insertion does not affect circuit functionality
Adding Elastic Buffers

## Slide 30
+
1
Br
Mg
  Buffer insertion does not affect circuit functionality
  Elastic buffers and circuit functionality
  Elastic buffers and avoiding deadlock
LD hist[x]
LD weight[i]
+
Buff
  r=0
  v=1
Adding Elastic Buffers

## Slide 31
LD hist[x]
LD weight[i]
+
Buff
+
1
Br
  Buffer insertion does not affect circuit functionality
Buff
  Elastic buffers and circuit functionality
  Elastic buffers and avoiding deadlock
Mg
  Each combinational loop in the circuit needs to contain at least one buffer
Adding Elastic Buffers

## Slide 32
LD x[i]
Mg
Fork
+
1
Start: i=0
Fork
Br
<
N
LD hist[x[i]]
LD weight[i]
St hist[x[i]]
+
Exit: i=N
Fork
Adding Elastic Buffers

## Slide 33
  2 Combinational loops
LD x[i]
Mg
Fork
+
1
Start: i=0
Fork
Br
<
N
LD hist[x[i]]
LD weight[i]
ST hist[x[i]]
+
Exit: i=N
Fork
Adding Elastic Buffers

## Slide 34
LD x[i]
Mg
Buff
Fork
+
1
Start: i=0
Fork
Br
<
N
LD hist[x[i]]
LD weight[i]
ST hist[x[i]]
+
Exit: i=N
Fork
Adding Elastic Buffers

## Slide 35
  Backpressure from slow paths prevents pipelining
Adding Elastic Buffers

## Slide 36
LD x[i]
Mg
Buff
Fork
+
1
Start: i=0
Fork
Br
<
N
LD hist[x[i]]
LD weight[i]
ST hist[x[i]]
+
Exit: i=N
Fork
Increasing Throughput

## Slide 37
LD x[i]
Mg
Buff
Fork
+
1
Start: i=0
Fork
Br
<
N
LD hist[x[i]]
LD weight[i]
ST hist[x[i]]
+
Exit: i=N
Fork
FIFO
FIFO
Increasing Throughput
  Insert FIFOs into slower paths

## Slide 38
Increasing Throughput
LD x[i]
Mg
Buff
Fork
+
1
Start: i=0
Fork
Br
<
N
LD hist[x[i]]
LD weight[i]
ST hist[x[i]]
+
Exit: i=N
FIFO
Fork
FIFO

## Slide 39
Join
Branch
Huang et al. Elastic CGRAs. FPGA ‘13.
  Sending multiple values to the next BB
Increasing Throughput
i
x
y

## Slide 40
Join
Branch
Huang et al. Elastic CGRAs. FPGA ‘13.
  Sending multiple values to the next BB
  Pipelining only with modulo scheduling
Increasing Throughput
x
y
i

## Slide 41
Join
Fork
Branch
Branch
Branch
Branch
  Pipelining only with modulo scheduling
Increasing Throughput
  Sending multiple values to the next BB
i
x
y
x
y
i

## Slide 42
Fork
Branch
Branch
Branch
  Pipelining without modulo scheduling
Increasing Throughput
  Sending multiple values to the next BB
i
x
y
Join
Branch
  Pipelining only with modulo scheduling
x
y
i

## Slide 43
Increasing Throughput
LD x[i]
Mg
Buff
Fork
+
1
Start: i=0
Fork
Br
<
N
LD hist[x[i]]
LD weight[i]
ST hist[x[i]]
+
Exit: i=N
FIFO
Fork
FIFO

## Slide 44
  What about memory?
LD x[i]
Mg
Buff
Fork
+
1
Start: i=0
Fork
Br
<
N
LD hist[x[i]]
LD weight[i]
ST hist[x[i]]
+
Exit: i=N
FIFO
Increasing Throughput
RAW dependency
not honored!
Fork
FIFO

## Slide 45
Connecting to Memory
  Load-store queue (LSQ)
    Needs information on the original program order of the memory accesses1
    Send tokens to the LSQ in order of basic block execution
1 Josipović et al. An out-of-order load-store queue for spatial computing. CASES ‘17.

## Slide 46
Connecting to Memory
LD x
LD weight
LD hist
ST hist
  Load-store queue (LSQ)
    Needs information on the original program order of the memory accesses1
    Send tokens to the LSQ in order of basic block execution
1 Josipović et al. An out-of-order load-store queue for spatial computing. CASES ‘17.
  LSQ
  Memory
  BB1 is starting
BB1: LD, ST

## Slide 47
Connecting to Memory
LD x
LD weight
LD hist
ST hist
  Load-store queue (LSQ)
    Needs information on the original program order of the memory accesses1
    Send tokens to the LSQ in order of basic block execution
1 Josipović et al. An out-of-order load-store queue for spatial computing. CASES ‘17.
  LSQ
  Memory
LD hist
ST hist
  BB1 is starting
BB1: LD, ST

## Slide 48
Connecting to Memory
LD x
LD weight
LD hist
ST hist
  Load-store queue (LSQ)
    Needs information on the original program order of the memory accesses1
    Send tokens to the LSQ in order of basic block execution
1 Josipović et al. An out-of-order load-store queue for spatial computing. CASES ‘17.
  BB1 is starting
  LSQ
  Memory
BB1: LD, ST
LD hist
ST hist
LD hist
ST hist

## Slide 49
Connecting to Memory
Dynamically scheduled circuit

## Slide 50
Connecting to Memory
Interface to the LSQ
Dynamically scheduled circuit
Fork

## Slide 51
Connecting to Memory
Interface to the LSQ
Dynamically scheduled circuit
Fork

## Slide 52
Outline
Introduction
Background: elastic circuits
Synthesizing elastic circuits
Evaluation
Conclusion

## Slide 53
Results
  Elastic designs dynamically resolve memory and control dependencies and produce high-throughput pipelines

## Slide 54
Results
  Elastic designs dynamically resolve memory and control dependencies and produce high-throughput pipelines

## Slide 55
Results
  Elastic designs dynamically resolve memory and control dependencies and produce high-throughput pipelines

## Slide 56
Results

## Slide 57
Results
Dynamically scheduled HLS is valuable for emerging FPGA applications

## Slide 58: Thank you!