## Slide 1
FPGA 2018
FASTCF: FPGA-based Accelerator for
STochastic-gradient-descent-based Collaborative Filtering
Shijie Zhou, Rajgopal Kannan, Min Yu, Viktor K. Prasanna

## Slide 2: Outline
Introduction
Optimizations and Accelerator Design
Experimental Results
Impact
Conclusion

## Slide 3: Recommender Systems
Information filtering system to predict the interest of users
Everywhere

## Slide 4: Collaborative Filtering
Apply machine learning algorithms to predict user’s rating for unrated items
  Bayesian networks
  Clustering
  Matrix factorization
    Stochastic gradient descent (SGD)
      Achieves high prediction accuracy
      Training is computation-intensive

## Slide 5: Problem Definition (1)
Input is a partially filled rating matrix
  # of users = # of rows = ||
  # of items = # of columns = ||

## Slide 6: Problem Definition (2)
Output contains two low-rank (i.e., ) matrices and
  : the row of (latent feature vector of user )
  the row of (latent feature vector of item )
  : the rating of given by

## Slide 7: Problem Definition (3)
Training process aims to find and that minimizes overall squared prediction error (i.e., )
SGD-based approach
Our focus
        Randomly initialize each and
        While not done do
          For each known rating do
        Update and based on
        End for
        End while
        Return and

## Slide 8: Challenges in Acceleration (1)
Feature vectors do not fit in on-chip memory of FPGA
How to achieve efficient data reuse?
Challenge 1
Memory
On-chip RAM
P
Q

## Slide 9: Challenges in Acceleration (2)
Feature vector dependencies
  Need to incrementally update feature vectors once per rating
Challenge 2

## Slide 10: Challenges in Acceleration (3)
Parallel processing units access on-chip RAMs
  Concurrent accesses to the same RAM  conflicts
How to reduce access conflicts?
Challenge 3
On-chip RAM
P
P
P
P

## Slide 11: Contributions
Novel optimizations to address the three challenges
  Partitioning and communication hiding
    Completely overlap communication with computation
  Parallelism extraction to reduce data dependencies by 28x – 60x
  Scheduling to reduce bank conflicts by 2x – 4x
  Sustain up to 217 GFLOPS for training large real-life datasets
Achieve 13.3x and 12.7x speedup compared with highly optimized multicore and GPU implementations
Generic technique to accelerate SGD-based training

## Slide 12: Outline
Introduction
Optimizations and Accelerator Design
Experimental Results
Impact
Conclusion

## Slide 13: Bipartite Graph Representation
1 | 
2 | 5
3.5 | 6
 | 4
1
2
4
3.5
5
User vertices
Items vertices
6

## Slide 14: Optimization 1 (1)
Graph Partitioning
1
2
4
3.5
5
1
2
5
6
4
3.5
6

## Slide 15: Optimization 1 (2)
Communication Hiding
  If
  the communication can be completely overlapped with the computation

## Slide 16
Objective: each subgraph should have sufficient edges for the computation to hide the communication
Fast heuristic partitioning approach
  Subset degree of a vertex subset
    number of edges that connect to the vertices in the subset
  Balance subset degrees of distinct vertex subsets
    Sort vertices based on vertex degree
    Greedy assignment of each vertex into the non-full vertex set that has the minimum subset degree
Optimization 1 (3)
Graph Partitioning and Communication Hiding

## Slide 17: Optimization 2
Partition the edges of each subgraph into non-overlapping matchings
  Edges in the same matching have no common vertices
Edge coloring
Parallelism Extraction

## Slide 18: Edge Scheduling
Partition the edges in each matching into batches
  Sort the edges based on the conflict index (i.e., the number of edges in the matching that have conflict with this edge)
  Assign each edge to the batch where its addition does not increase the conflicts within the batch
Optimization 3

## Slide 19: Architecture of FASTCF
Multi-ported RAM based on banking
Check FV dependencies based on fine-grained locking
Parallel processing units to process distinct edges
Resolve bank conflicts to feature vector buffer

## Slide 20: Outline
Introduction
Optimizations and Accelerator Design
Experimental Results
Impact
Conclusion

## Slide 21: Experimental Setup
Real-life datasets
Virtex UltraScale+ xcvu9pflgb2104 FPGA (for training)
  43 MB of on-chip RAM
Intel Xeon E5-2686 processor (for pre-processing)
  8 cores @ 2.3 GHz
Dataset | # users | # items | # ratings | Description
Libim | 135 K | 168 K | 17,359 K | Dating ratings
Netflix | 480 K | 17 K | 100,480 K | Movie ratings
Yahoo | 1,200 K | 136 K | 460,380 K | Music ratings
Notes: DDR3 bandwidth 15 GB/s

## Slide 22: Pre-processing Overhead
Dataset |  |  |  |  | 
Libim | 0.4 sec | 4.4 sec | 2.7 sec | 7.5 sec | 2.1%
Netflix | 1.0 sec | 10.7 sec | 7.0 sec | 18.7 sec | 2.1%
Yahoo | 5.5 sec | 42.3 sec | 23.0 sec | 70.8 sec | 2.8%
Dataset |  |  |  |  | 
Libim | 0.4 sec | 4.4 sec | 2.7 sec | 7.5 sec | 2.1%
Netflix | 1.0 sec | 10.7 sec | 7.0 sec | 18.7 sec | 2.1%
Yahoo | 5.5 sec | 42.3 sec | 23.0 sec | 70.8 sec | 2.8%
Pre-processing overhead can be amortized since the training is iterative
=

## Slide 23: Performance vs. Parallelism
Chart: 
| 1 | 2 | 4 | 8
Libim | 42 | 88 | 133 | 165
Netflix | 46 | 92 | 161 | 213
Yahoo | 47 | 93 | 163 | 217
Number of parallel processing units ()
Throughput (GFLOPS)
47
217
93
163
Notes: performance of Bank-conflict-free design deteriorates due to 2 reasons:
1. lower clock rate for larger 𝐾
2. Smaller capacity of on-chip buffer for larger 𝐾  small matchings  low parallelism

## Slide 24: Impact of Optimization 1
Communication Hiding
Data set | per iteration (sec) |  | Speedup
 | Opt. | Base. | 
Libim | 0.03 | 0.04 | 1.3x
Netflix | 0.15 | 0.16 | 1.1x
Yahoo | 0.68 | 0.76 | 1.1x
Data set |  |  | Speedup
 | Opt. | Base. | 
Libim | 0.03 | 0.04 | 1.3x
Netflix | 0.15 | 0.16 | 1.1x
Yahoo | 0.68 | 0.76 | 1.1x
Optimized design: Opt 1 + Opt 2 + Opt 3
Baseline design: Opt 2 + Opt 3

## Slide 25: Impact of Optimization 2
Pipeline stall reduction
Data set | Pipeline stalls due to dependencies |  | Reduction | per iteration (sec) |  | Speedup
 | Opt. | Base. |  | Opt. | Base. | 
Libim | 2,005 K | 57,524 K | 28.7x | 0.03 | 0.40 | 13.3x
Netflix | 6,151 K | 314,884 K | 51.2x | 0.15 | 2.19 | 14.6x
Yahoo | 24,954 K | 1,500,295 K | 60.1x | 0.68 | 10.45 | 15.4x
Data set | Pipeline stalls due to dependencies |  | Reduction |  |  | Speedup
 | Opt. | Base. |  | Opt. | Base. | 
Libim | 2,005 K | 57,524 K | 28.7x | 0.03 | 0.40 | 13.3x
Netflix | 6,151 K | 314,884 K | 51.2x | 0.15 | 2.19 | 14.6x
Yahoo | 24,954 K | 1,500,295 K | 60.1x | 0.68 | 10.45 | 15.4x
Optimized design: Opt 1 + Opt 2 + Opt 3
Baseline design: Opt 1 + Opt 3

## Slide 26: Impact of Optimization 3
Bank conflict reduction
Data set | Bank conflicts |  | Reduction | per iteration (sec) |  | Speedup
 | Opt. | Base. |  | Opt. | Base. | 
Libim | 1,165 K | 2,798 K | 2.4x | 0.03 | 0.04 | 1.3x
Netflix | 3,960 K | 16,686 K | 4.2x | 0.15 | 0.23 | 1.5x
Yahoo | 19,393 K | 75,524 K | 3.9x | 0.68 | 1.03 | 1.5x
Data set | Bank conflicts |  | Reduction |  |  | Speedup
 | Opt. | Base. |  | Opt. | Base. | 
Libim | 1,165 K | 2,798 K | 2.4x | 0.03 | 0.04 | 1.3x
Netflix | 3,960 K | 16,686 K | 4.2x | 0.15 | 0.23 | 1.5x
Yahoo | 19,393 K | 75,524 K | 3.9x | 0.68 | 1.03 | 1.5x
Optimized design: Opt 1 + Opt 2 + Opt 3
Baseline design: Opt 1 + Opt 2

## Slide 27: Comparison with State-of-the-art
Approach | Platform | Processor Power | Exec. Time per Iteration | Speedup
SIGMOD ’14 | 24-core Intel E5-2697 | 130 W | 2.00 sec | 13.3x
This paper | Virtex UltraScale+ | 14 W | 0.15 sec | 
GPGPU ’15 | 2880-core Tesla K40C GPU | 235 W | 1.90 sec | 12.7x
This paper | Virtex UltraScale+ | 14 W | 0.15 sec | 
Up to 13.3x speedup for training the Netflix dataset

## Slide 28: Outline
Introduction
Optimizations and Accelerator Design
Experimental Results
Impact
Conclusion

## Slide 29: Impact of This Work
Accelerate other data science problems that derive latent features from observations
  Topic modeling/extraction
  Word embedding
Techniques for accelerating SGD-based training algorithms
Generic optimizations applicable to other platforms

## Slide 30: Conclusion
Developed FASTCF to accelerate SGD-based CF
Designed three optimizations to
  completely overlap communication with computation
  reduce data dependencies to extract parallelism
  reduce bank conflicts
Achieved a high throughput of up to 217 GFLOPS for training large real-life datasets
Achieved 13.3x and 12.7x speedup compared with state-of-art multicore and GPU implementations

## Slide 31
Comments & Questions
Thank you
fpga.usc.edu