## Slide 1
Sean Fox, David Boland and Philip H.W. Leong
School of Electrical and Information Engineering,
The University of Sydney
FPGA Fastfood – A High Speed
Systolic Implementation of an Online
Kernel Method
Notes: 1
This talk is about a computationally inexpensive machine learning algorithm, which we have used to scale up implement

## Slide 2
Online Kernel Methods
f(x)
∑
Update
Unknowns
prediction
yi
xi
d, α
+
-
“Kernel Method” →
Dictionary → subset of the input data of length N
Computation and Memory scale O(Nd)
BUT… N scales linearly with the dataset size
Dictionary Entry
Notes: Our implementation of Fastfood is a type of Online Kernel Method, online meaning that we do training and prediction, and kernel method meaning that the kernel trick is used to extract non-linear relationships inexpensively.

## Slide 3
Exact Kernel Methods
Random Kernel Expansion
** Only for k(x,x’) = k(x-x’,0)
  Define z(x):
1 x d
1 x n
z(x)
α
Output
Input
Approximates
MV + Non-Linear Activation
(i.e. like Multilayer Perceptron)
W is fixed and random
Random Approximation
(Rahimi and Recht, ‘07)

## Slide 4
B, G, S
P
0 0 1 0
1 0 0 0
0 0 0 1
0 1 0 0
H
1 1 1 1
1 -1 1 -1
1 1 -1 -1
1 -1 -1 1
Fast Hadamard Transform (dxd)
Memory = O( 3n )
Time = O( n log d )
** Each Qjx is an independent dxd transform
Computes z(x) efficiently by replacing Wx with combinations of random diagonal matrices and Hadamard transforms
Fastfood
(Le et al. ‘13)

## Slide 5
Systolic Array Architecture
HBh
HB2
HB1
HBh-1
HB3
HB4
Top
PE2
PEb
PE1
SWITCH
SUM & UPDATE
inBuff
+
x
-
RAM
CTRL
RAM
LFSR
HB
PE
Block of b PEs (i.e. )
General PE: 18-bit ALU, RAMs, Control Unit, LFSR
Notes: An interesting aspect of this architecture is the hardware reuse. The same PEs do all the computation in Fastfood. This includes the switching/buffering for the Hadamard transform, and the elementwise stuff,

## Slide 6
Results and Conclusion
6
Supports much larger problems
High speed design
245x speed-up over a CPU
Impl. | dim. | n | bw | Lat. (cyc) | Fmax (MHz) | Exec (ns) | Th.put (Gb/s)
NORMA (V7, ‘15) | 8 | 200 | 18 | 10 | 127 | 7.87 | 18.3
KNLMS (V7, ‘15) | 8 | 16 | 32 | 207 | 314 | 3.18 | 80.4
CPU (Le et. ‘13) | 1024 | 16.4k | 32 |  |  | 58e4 | 0.06
FASTFOOD (V7) | 1024 | 16.4k | 18 | 1893 | 432 | 23.7e3 | 7.77
FASTFOOD (KU035) | 8192 | 90.1k | 18 | 16930 | 508 | 17.2e3 | 8.57