## Slide 1
EdgeSort: A Sub-100 ns, Line-Rate FPGA Streaming Sorter
Greg Stitt, Wesley Piard, Christopher Crary
Department of Electrical and Computer Engineering
University of Florida
FPGA 2026

## Slide 2: Introduction
Most prior sorting work focused on maximizing throughput
  Streaming applications constrained by network bandwidth
  New opportunity for low-latency sorting
GPUs are not well-suited for low-latency streaming applications
  Latency dominated by PCIe times, even for infinitely fast throughput
Stream In
PCIe Write
PCIe Read
Stream Out
High-Throughput Sort (e.g., GPU)
Latency Increase over Ideal
Stream In
Stream Out

## Slide 3: EdgeSort
We introduce EdgeSort for SmartNIC FPGAs
  Lower throughput than GPUs, but:
    Achieves line-rate sorting at common networking bandwidths
    Minimizes 1) latency to first output, and 2) total added latency over ideal
  Two orders of magnitude lower latency than PCIe accelerators
  ~100 Gbps throughput with < 100 ns of added latency for 128k-element arrays
Stream In
PCIe Write
PCIe Read
Stream Out
Stream In
Subsorting
Stream Out
Merging
High-Throughput Sort (e.g., GPU)
Lower-Throughput Streaming Sort (EdgeSort)
Orders-of-magnitude latency improvement
Latency to First Output
Stream In
Stream Out
Total Added Latency

## Slide 4: Architecture Overview
Architecture based on common subsort-merge strategy
Input Distributor
Parallel Tournament Tree
8,2
5,3
2,4
6,1
6
5
3
1
8
2
4
2
Scatters inputs to parallel sub-sorts
Parallel sub-sorts
. . . . . . . . . . . .

## Slide 5: Architecture Overview
Input Distributor
Parallel Tournament Tree
6
3
8
4
5
1
2
2
1,2,2
Parallel sub-sorts
Tree merges sorted sub-arrays faster than input arrival rate, guarantees line-rate
. . . . . . . . . . . .
Architecture based on common subsort-merge strategy

## Slide 6: Architecture Overview
Input Distributor
Parallel Tournament Tree
5
3
8
4
3,4,5
1,2,2
6
Parallel sub-sorts
. . . . . . . . . . . .
Architecture based on common subsort-merge strategy
Tree merges sorted sub-arrays faster than input arrival rate, guarantees line-rate

## Slide 7: Architecture Overview
Input Distributor
Parallel Tournament Tree
6
8
6,8
3,4,5
1,2,2
Architecture based on common subsort-merge strategy
Tree merges sorted sub-arrays faster than input arrival rate, guarantees line-rate
Parallel sub-sorts

## Slide 8: EdgeSort Architecture
Extends common strategy with optimizations for scalability and latency
Line-Rate FIFO
Input Distributor
Output FIFO
HSSH-1
HSS0
HSS1
Parallel Tournament Tree
a[i..i+Pin-1]
PFIFO
1 to PTT outputs
b[i..i+Pout-1]
. . . . . . . . . . . . .
k
Buffers next array while sub-sorts drain
H hybrid sub-sorts of k elements each provide initial sorted burst, then reduce throughput to improve scalability
Output FIFO coalesces merged outputs into beats of output bus width
Parallel tournament tree provides sufficient (not max) throughput for line-rate to reduce resources and latency
For k=1024, each HSS requires 1 BRAM
H=1024: 1M element arrays with 1024 BRAMs, 784k LUTs

## Slide 9: Input Distributor
Scatters Pin inputs every cycle to H hybrid sub-sorts (HSS)
  Shown for Pin=2
Uses a tagged “conveyor”
  Tag specifies ID of HSS to use
  Shift register acts as conveyor
  HSS accepts any element whose tag matches ID
Two tagging methods
  Counter: simple, but not ideal for some distributions
  LFSR: randomizes assignment to improve parallelism in tournament tree
a0
HSS0
Tag == 0
HSS1
Tag == 1
HSS0
Tag == 2
HSS1
Tag == 3
HSSH-1
Tag == H-1
Tag Assignment
Counter/LFSR
a1
From line-rate FIFO
. . . . . . . .
. . . . . . . .
. . . . . . . .
To parallel tournament tree

## Slide 10: Hybrid Sub-Sorts (HSS)
Provides sub-sorting with combination of sorting methods
Optimized for throughput demands of tournament tree
  Children of root read from with probability ½
  Grand-children of root read from with probability ¼
  Nodes at depth n read from with probability 1/2n
For tournament tree with T inputs, read probability of each input is 1/T
  Low throughput requirements => can save resources to improve scalability
Heap sort in BRAM is area efficient, meets throughput constraint
  But, can have latency of > 30 cycles for 1024-element RAM
Problem: poor latency when filling tournament tree pipeline

## Slide 11: Hybrid Sub-Sorts (HSS)
Solution: use faster sort initially (insertion sort)
  Burst buffer provides initial sorted burst every cycle to quickly fill tree pipeline
    Doesn’t scale to large sizes, but doesn’t need to
Switch to scalable buffer (heap sort) after pipeline filled
End-of-stream buffer to avoid 30+ cycle latency of inserting last array element into heap
  HSS can feed tournament tree immediately after receiving last element
Burst Buffer
(Insertion Sort)
Scalable Buffer
(Heap Sort)
End-of-Stream Buffer
(Register)
element
ready
Input FIFO
Output FIFO
FIFO Read Logic
rd_en
empty
write enables
(for each buffer)
drain
Read Controller
Write Controller
eviction

## Slide 12: Parallel Tournament Tree
Tournament tree must output data at least as fast as inputs arrive (required for line rate)
  Previous work has introduced parallel mergers, but require massive resources
  We aren’t maximizing throughput, just achieving enough for line-rate
Introduced a novel parallel tournament tree
  Uses PTT separate sequential trees
  Challenge: need to see deeper than the root of each tree
. . . .
. . . .
1 3 7 9
0 2 4 8
. . . .
. . . .
5 6 7 9
0 2 4 8
. . . .
. . . .
8 8 9 9
0 2 4 8
Can only read 1 element
Can read 3 elements
Can read 4 elements
Tree0
Tree1
Tree2
Tree3
Tree0
Tree1
Tree2
Tree3
Tree0
Tree1
Tree2
Tree3
Ordering Rule:
  Can read from tournament tree i, only if besti <= nextj, for all j in 0 to PTT-1
  Guarantees 1 output per cycle, up to PTT outputs every cycle

## Slide 13: Parallel Tournament Tree
Lookahead FIFOs
  Provides best and next elements for all trees
Order analyzer verifies ordering rule for each tree
Sorting network
  Odd-even mergesort sorting network
  Sorts PTT elements each cycle
  Elements not read from tree are ignored
Variable-write FIFO
  Accepts between 1 and PTT sorted elements
  Outputs PTT elements
  Uses pipelined barrel shifting
best0
next0
Sequential Tournament Tree 0
h0
Lookahead FIFO
Order Analyzer
Sorting Network
done0
bestPTT-1
nextPTT-1
Sequential Tournament Tree PTT-1
Lookahead FIFO
donePTT-1
best0
valid0
bestPTT-1
validPTT-1
best1
valid1
. . . . . . . . . . . . . .
. . . . . . . . . . . . . .
. . . . . . . . .
h1
hH/PTT-1
. . . . . . . . . . . . . .
hH-PTT
hH-1
. . . . . . . . . . . . . .
hH-PTT+1
best[i..i+PTT -1]
valid_count
rd_en0
rd_enPTT-1
Variable-Write FIFO
b[i..i+PTT -1]

## Slide 14: Latency Analysis
best0
next0
Sequential Tournament Tree 0
h0
Lookahead FIFO
Order Analyzer
Sorting Network
done0
bestPTT-1
nextPTT-1
Sequential Tournament Tree PTT-1
Lookahead FIFO
donePTT-1
best0
valid0
bestPTT-1
validPTT-1
best1
valid1
. . . . . . . . . . . . . .
. . . . . . . . . . . . . .
. . . . . . . . .
h1
hH/PTT-1
. . . . . . . . . . . . . .
hH-PTT
hH-1
. . . . . . . . . . . . . .
hH-PTT+1
best[i..i+PTT -1]
valid_count
rd_en0
rd_enPTT-1
Variable-Write FIFO
b[i..i+PTT -1]
log2(H) cycles, <= 10
2 cycles
1+ cycles
1+ cycles
log2(PTT) cycles,
1 to 15 for PTT = 1 to 32
Total cycles: 15 to 29

## Slide 15: Latency Analysis
1+ cycles
Total cycles: 19 to 33
Line-Rate FIFO
Input Distributor
Output FIFO
HSSH-1
HSS0
HSS1
Parallel Tournament Tree
a[i..i+Pin-1]
PFIFO
1 to PTT outputs
b[i..i+Pout-1]
. . . . . . . . . . . . .
k
1+ cycles
1 cycle during initial burst
15 to 29 cycles
1+ cycles
15

## Slide 16: Parallel Tournament Tree
Evaluated parallelism of tree
  Varied max potential parallelism PTT
  Measured mean outputs per cycle
  Tested 6 distributions
  128 inputs (max array size: 128k)
Diminishing returns with larger PTT
  Achieved ~7-8 outputs/cycle at PTT=32
  Similar results across distributions

## Slide 17: Scalability Experiments
Setup:
  Bus width: 32 to 512
  32-bit key, rest is data
  PTT=2
  Maximum size: 128k elements
  1.7M LUT Versal device
Bandwidth: 11.2 to 98.8 Gbps
  Primarily limited by decrease in clock
Clock: 349 MHz to 193 MHz
  Easy to improve clock at cost of latency
Latency: 74 ns to 134 ns
  Same for latency to first output and total added latency (no gaps)

## Slide 18: Resource Utilization
PTT=2, maximum size of 128k elements
Evaluated for 1.7M LUT Versal
BRAM bottleneck for wide buses
  Could be improved with UltraRAM
  Other alternatives for low-area, low-PTT data steering in paper

## Slide 19: Latency Improvement
Compared EdgeSort latency to PCIe Gen 4 x16 acceleration
  Assumes maximum possible bandwidth (31.5 GB/s) and infinitely fast computation
  Results pessimistic because small PCIe transfers have low bandwidth
EdgeSort achieves > 100x latency improvements for arrays above 32k

## Slide 20: Conclusion
We introduced EdgeSort architecture for SmartNIC FPGAs
  Achieved latencies under 100 ns for arrays up to 128k elements
  Line-rate sorting for common bandwidths (up to 98.8 Gbps)
  Showed scalability up to 1M elements
Achieved 1-2 order-of-magnitude latency reductions compared to PCIe accelerators
Hybrid sub-sort and parallel tournament tree designed specifically to reduce latency