## Slide 1: AI-Assisted Copilot Automation for Reliable FPGA Verification at Hyperscale
Linh Nguyen, Nguyen Le, Tony-Dat Tran, Jagannath Panduranga Rao, Andrew Putnam Microsoft Corporation ISFPGA ’26, Seaside, CA, USA
Notes: AI-generated content may be incorrect. ---

## Slide 2: Introduction & Motivation​
Hyperscale FPGAs require robust verification​
Simulation-only flows miss corner cases​
Formal methods offer exhaustive checking​
Complex reset mechanisms in FPGAs​
Azure Boost case study with PCIE Functional Level Reset (FLR) with 32 Physical Functions (PF) and 1028 Virtual Functions (VF)​ for each PF
Notes: --- This slide references information from the following file: https://microsoft-my.sharepoint.com/personal/nguyenlinh_microsoft_com/Documents/Microsoft%20Teams%20Chat%20Files/FPGA_2026__Industry_Track__F236.pdf AI-Assisted Copilot Automation for Reliable FPGA Verification at Hyperscale Linh Nguyen Microsoft Corporation Mountain View, CA, USA nguyenlinh@microsoft.com
Nguyen Le Microsoft Corporation Mountain View, CA, USA ngle@microsoft.com
Tony-Dat Tran Microsoft Corporation Mountain View, CA, USA tonytran@microsoft.com Jagannath Panduranga Rao Microsoft Corporation Mountain View, CA, USA japandur@microsoft.com
Andrew Putnam Microsoft Corporation Redmond, WA, USA anputnam@microsoft.com Abstract Cloud-scale, Artificial Intelligence (AI)-centric deployments are increasingly accelerated andmade flexible through Field-Programmable Gate Arrays (FPGAs). Traditional simulation-only verification has often been shown to miss system-level risks that surface late during hardware bring-up. A hybrid verification methodology has therefore been developed in which AI-driven automation is orchestrated with formal connectivity checks to ensure reliable end-to-end signal connectivity and robust reset behavior across heterogeneous FPGA Stock Keeping Unit (SKU) variants. Structured prompts are employed to guide Copilot in generating Python scripts that traverse - Register Transfer Level (RTL) designs, extract signal mappings, and auto-generate timing-aware connectivity assertions in Comma-Separated Values (CSV) format. Precise, context-rich prompts specifying signal roles, hierarchy depth, and reset domains are observed to yield consistent results, whereas generic prompts fail to capture architectural nuances. Reset validation strategies covering Function Level Resets (FLRs), Memory-Mapped Input Output (MMIO) handlers, and firmware-driven resets have been applied in FPGA contexts, while the underlying connectivity assertion framework has been shown to be portable to Application-Specific Integrated Circuit (ASIC) flows with minimal adaptation. Over nine months, the methodology was deployed on multiple hyperscale FPGA platforms, where critical bugs missed by weeks of simulation regressionswere surfaced. Integrationwith commercial formal tools was achieved, scalability to new FPGA variants was demonstrated, and lessons in prompt engineering and cross-domain verification were documented. CCS Concepts • FPGA ; • Hardware →Reconfigurable logic applications; • Computer systems organization →Reconfigurable computing; Heterogeneous (hybrid) systems;
This work is licensed under a Creative Commons Attribution 4.0 International License. FPGA ’26 February 22–24, 2026, Seaside, CA, USA © 2026 Copyright held by the owner/author(s). ACM ISBN 979-8-4007-2079-6/2026/02 https://doi.org/10.1145/3748173.3779205
Keywords FPGA reliability; formal connectivity verification; resets verification; Copilot assisted automation; cloud/hyperscale deployments; verification productivity ACM Reference Format: Linh Nguyen, Nguyen Le, Tony-Dat Tran, Jagannath Panduranga Rao, and Andrew Putnam. 2026. AI-Assisted Copilot Automation for Reliable FPGA Verification at Hyperscale. In Proceedings of the 2026 ACM/SIGDA International Symposium on Field Programmable Gate Arrays (FPGA 2026), February 22–24, 2026, Seaside, CA, USA. ACM, New York, NY, USA , 10 pages. https://doi.org/10.1145/3748173.3779205 1 Introduction Modern cloud infrastructure increasingly incorporates FPGAs to accelerate networking, storage, and AI workloads [1]. Ensuring hyperscale reliability in such FPGA deployments is challenging because even small connectivity errors or reset sequencing bugs can cause system-wide failures. Traditional verification flows rely heavily on simulation testbenches, which are labor-intensive to create and may not cover all corner cases, especially for resets and rarelytoggled signals. In contrast, formal verification techniques, such as connectivity checking, can exhaustively prove signal hookups and uncover corner-case issues early. However, applying formal methods at scale requires well-defined connectivity specifications, which are tedious to write and maintain manually. Moreover, in FPGA-based systems, the reconfigurable and firmware-interactive reset mechanisms (e.g. Function Level Reset (FLR), hot reset, partial reconfiguration (PR)) introduce additional complexity not present in ASIC flows. Key challenge: As a concrete example, our team faced verification of a complex FPGA design as part of Microsoft Azure Boost [2] featuring 32 Physical Functions (PFs), each supporting up to 1028 Virtual Functions (VFs) on a single device. This design included numerous resets with the combination of PFs and VFs (FLR), or hot resets, soft resets across different power domains and required consistent connectivity between a custom MMIO Handler block and various Peripheral Component Interconnect Express (PCIe) and a system that offloads virtualization and host OS functions(hereafter referred to as the Shell) interfaces. Weeks of simulation on this design still left gaps in coverage, motivating a more exhaustive solution. Our solution: A hybrid verification flow was developed that combines Image source: AI-generated

## Slide 3: Hybrid Verification Workflow
Step 1: Structured Prompts​
Step 2: Copilot Script Generation​
Step 3: Formal Engine (QCC)​
Step 4: Simulation in Block Level /Protosim​
Step 5: Iterative Refinement​
Notes: --- This slide references information from the following file: https://microsoft-my.sharepoint.com/personal/nguyenlinh_microsoft_com/Documents/Microsoft%20Teams%20Chat%20Files/FPGA_2026__Industry_Track__F236.pdf
FPGA ’26 February 22–24, 2026, February 22–24, 2026, Seaside, CA, USA Linh Nguyen, Nguyen Le, Tony-Dat Tran, Jagannath Panduranga Rao, and Andrew Putnam AI-assisted automation with formal connectivity checking to address this problem. Copilot [3] , a large-language-model-based coding assistant, was employed to automatically generate verification scripts from high-level prompts derived from design specifications and engineering discussions. These scripts were then used to drive a formal connectivity checking tool (Siemens Questa Connectivity Check, QCC [4]), enabling exhaustive verification of both static connections and reset propagation paths. The flow was refined iteratively over a nine-month period and deployed across multiple generations of hyperscale FPGA platforms, leading to significant improvements in bug discovery and time-to-bring-up. In the remainder of this paper, the approach and contributions are described. • Section 2: Methodology and Prompt Engineering: The orchestration of Copilot with formal tools is described, including examples of effective and ineffective prompts for script generation and the limitations of AI (Copilot and other large-language models) in verification workflows. Emphasis is placed on prompt engineering, structured prompt interpretation across models, and quantitative comparisons between simulation-only and hybrid flows. • Section 3: FPGA vs. ASIC Considerations: Which aspects of our flow are specific to FPGA (reconfigurable resets, SKU variability) and which generalize to ASIC verification. • Section 4: Deployment and Results: An AI-assisted formal verification flow was deployed across FPGA projects, with adoption scope, development effort, and bug-finding outcomes highlighted. Over a nine-month period, connectivity checks were accelerated through Copilot, critical reset and wiring bugsmissed by simulationwere uncovered, first-time-right bring-up was enabled, and structural bottlenecks were eliminated, thereby boosting productivity while maintaining a focus on functional verification. • Section 5: Comparison with Existing Solutions: How our AI-assisted approach differs from or complements tools like OneSpin’s connectivity app [5] and Cadence JasperGold [6]. • Section 6: Future Directions: Expanding the methodology to protocol verification, documentation automation, multi-die systems, and cross-domain scenarios. • Section 7: Conclusion: AI-assisted formal verification framework that improves coverage and efficiency for hyperscale FPGA systems by combining Copilot-generated scripts with formal tools and emulation, catching subtle bugs early and reducing manual effort. This human-in-the-loop approach shows that large language models can significantly enhance hardware verification when guided by precise prompts, offering a scalable blueprint for future FPGA and ASIC projects. • Appendix: Prompt examples and corresponding PythonCopilot assisted script 2 Methodology: AI-Orchestrated Formal Verification Flow Our methodology tightly integrates an AI assistant [3]with formal verification to achieve thorough connectivity and reset checking. Figure 1 illustrates the overall orchestration of Copilot[7] + QCC(Questa Connect Check)[4] + Protosim (prototype simulation
environment) in our flow, and we describe each component in detail below.
Figure 1: Workflow combining Copilot, QCC, and Protosim for connectivity & reset verification. Structured prompts (left) guide Copilot to generate Python scripts and CSV specifications, which feed into formal engine. In parallel, Copilot helps create reset test stimuli for (FPGA simulation). Formal counterexamples or simulation discrepancies (dashed arrows) are fed back to refine the prompts, iterating until all checks pass 2.1 Copilot-Generated Verification Scripts Central to our approach is using Copilot to generate custom verification collateral. We crafted structured prompts describing what we need to verify, and Copilot produced Python scripts accordingly. Key elements of successful prompts included: • Explicit Hierarchy and File Context: We specify the design hierarchy to search (e.g. Shell top-level vs. MMIO Handler submodule) and provide Copilot with links or paths to relevant source files (e.g. Shell.sv, MmioHandler.sv). This guides the code generator to the right modules. • Desired Output Format: We instruct Copilot to output results as a CSV, with defined column headers for source signal, destination signal, condition, delay, reset domain, polarity, clock, etc. (matching QCC’s expected input). By including a schema or example in the prompt, we got consistent CSV generation. • Context from Specifications and Discussions: We often paste snippets of design specifications (e.g. connectivity requirements like “A connects to C through B with certain delay”) and even relevant email threads into the prompt. Copilot can then infer intended connections or signal groupings. For example, stating “Based on document X (A < B < C) create connections between BlockA.signalA and BlockC.signalC with appropriate reset and clock domain” led Copilot to code a loop that pairs signals accordingly. • Reset Semantics: We clarify reset signal names and polarities (active-high or active-low) up front. In earlier attempts, forgetting to mention reset polarity led to incomplete checks. By adding something like “assume reset_n means activelow” in the prompt, the script correctly handles inversion conditions.
AI-Assisted Copilot Automation for Reliable FPGA Verification at Hyperscale FPGA ’26 February 22–24, 2026, February 22–24, 2026, Seaside, CA, USA Using these techniques, Copilot generated Python scripts that parse RTL netlists, traverse connectivity from sources to sinks, and emit CSV lines for each connection or reset path. These scripts effectively encode the connectivity specifications needed by formal tools, saving us fromwriting hundreds of assertions or connectivity rules manually. Notably, because prompts capture high-level intent, the scripts remained resilient to minor RTL changes—up to a point, we could regenerate the connectivity specifications after design refactors simply by re-running Copilot with an updated prompt. AI-assisted tools like GitHub Copilot accelerate Python development by generating context-aware code, reducing boilerplate, and enabling rapid prototyping. This boosts productivity and lowers entry barriers for non-experts. However, Copilot-generated scripts may include inefficiencies, redundant logic, or subtle errors, raising concerns about maintainability and security. Manual scripting, while time-intensive, ensures precision, optimized performance, and adherence to coding standards, fostering deeper understanding and long-term reliability. A balanced approach—using Copilot for scaffolding and manual refinement for correctness—offers speed without sacrificing quality, making it ideal for enterprise-grade software development. Example Prompt and Result: Listing 1 in Appendix shows a redacted prompt we used to generate reset connectivity checks, and the resulting snippet of Python code. In summary, Copilot was able to interpret instructions like “traverse all signals matching mmio_req in Shell → follow through to pcie.mmio_if* in Core; consider any enable signals or pipeline stages (1-cycle delay) along the path; output CSV”* and produce a working script. This level of automation freed engineers from writing boilerplate code and allowedmore focus on reviewing results and analyzing corner cases. 2.2 Formal Connectivity and Reset Checking We leveraged Questa Connectivity Check (QCC) – a formal verification app by Siemens – as the engine to prove connectivity assertions. QCC can exhaustively verify that for every specified source-destination pair, there exists a valid signal path (static or conditional) in the design, and conversely that no unexpected connections exist. It automatically generates SystemVerilog Assertions (SVAs) from a given specification (CSV or XML) and uses formal solvers to check them. In our flow, the CSV produced by Copilot’s script becomes the input specification for QCC. Each row represents either a direct static connection or a conditional connectivity requirement, possibly with an allowed pipeline delay or condition expression. We found QCC robust in handling our 4K connectivity checks per PF, completing proofs in hours per block, versus weeks if we attempted to cover all combinations in simulation. This aligns with literature reports that formal connectivity apps can cover scenarios in hours that would take weeks via testbenches. Adapting QCC for Reset Paths: A novel aspect of our work was encoding reset sequences as a form of connectivity so that QCC can verify them. Typically, connectivity apps ensure that signal A is connected to B (possibly through combinational logic or buses) under certain conditions, but resets involve temporal behavior (assert reset, then see effect somewhere else). We modeled each reset domain as having a source (reset initiator) and destinations (flip-flops or blocks that should receive the reset). By treating the assertion
"ResetX of BlockA travels through ResetControllerY and reaches BlockZ within 1 cycle" similarly to a connectivity specification (source=ResetX, dest=BlockZ.reset_pin, cond_expr="after 1 cycle" etc.), we got QCC to formally verify reset propagation. While not a built-in use of the tool, this worked because resets in our FPGA design were primarily synchronous and thus mappable to connectivity with a known latency. We also utilized QCC’s support for temporal/sequence checks for cases where a reset had to propagate through asynchronous crossings (modeling that as a two-step connection). This approach allowed formal, exhaustive checking of resets like FLR across 1028 VFs – something infeasible with pure simulation. Crucially, the integration between Copilot scripts and QCC was seamless: whenever an assertion failed, QCC provided a counterexample waveform (e.g., a missing connection or an unexpected path). We would feed this feedback to refine the prompts. For instance, an initial specification might omit that a multiplexor in the path needs a certain config bit set; QCC finds the unconnected scenario, and we then update the prompt to include that condition in the CSV (or to instruct Copilot to fetch that configuration from the RTL). This feedback loop converged in a few iterations for each block. 2.3 Dynamic Validation with Protosim While formal tools excel at static and sequential logic checks, they cannot directlymodel software or firmware interactions that trigger resets. To cover scenarios like firmware-initiated FLRs or partial reconfiguration, we incorporated Protosim (an FPGA prototyping/simulation hybrid platform) to run actual reset sequences in a cycle-accurate model of the system. Copilot also aided here: we prompted it to generate test cases (stimulus sequences) for Protosim that perform resets on all PFs and random subsets of VFs, mimicking real-world use. We ran these scenarios to observe any functional issues (e.g., a VF not resetting correctly because a firmware register wasn’t hooked up to hardware). Whenever Protosim revealed a discrepancy, we traced it to either the specification (prompt) or the design and fixed it accordingly. The combination of QCC and Protosim gave us confidence both in structural correctness (formal proof that connectivity and resets can work) and in dynamic behavior (evidence that they do work in a near-real environment). In practice, Protosim runs also served to validate that the formal environment assumptions (like reset latency = 1) were accurate. 2.4 Prompt Engineering: Lessons Learned Our experience highlighted how critical it is to engineer prompts thoughtfully when using AI in EDA workflows: Formal Connectivity Check Prompts (MMIO Handler and TestClient). Goal: Verify that every intended signal connection between the MMIO Handler and the TestClient is present and correct. This includes: • Data paths • Ready/valid handshakes • Gating conditions (e.g., enable signals) Prompt Structure: A prompt for this use case explicitly names the source and sink of the connection and any intermediate logic. For example, one successful prompt was:

## Slide 4: AI-Driven Verification via Copilot Prompts
Engineers write explicit and structured prompts​
Copilot generates Python scripts & CSV files​
Saves time and ensures consistency​
Model | Typical Behavior with Structured Promts | Recommended Mitigation Strategies
ChatGPT | Strict format adherence; May add extra nesting or verbose lists | Use explicit key constraints; validate with JSON schema; lower temperature
Gemini | Reorders keys; may insert summary comments | Provide one-shot examples; Enforce schema; Post-process with validator
Claude | Adds explanatory text Occasionally omits minor fields | Strong “JSON-only” directive Use JSON mode Automated format checks

## Slide 5: Formal Connectivity & Reset Verification
The commercial tools excel at performing the formal analysis quickly and at very large scale; formally proves source-destination signal paths​
Provide convenient debug environments for tracing failures
In Azure Boost found 4,000+ assertions per PF​
Resets modeled as connectivity​ from source to destination

## Slide 6: Dynamic Reset Validation ​
Use AI to automate and maintain the connectivity and to extend it into the realm of reset verification in simulation
Copilot leans on the formal connectivity feedback/results to generate test sequences, assertions​
Simulation validates real-world reset behavior​

## Slide 7: Prompt Engineering – Key Lessons
Be specific and structured​
Provide output examples​
Iterate and refine​
Maintain human oversight and use formal tool /simulation as baseline to prevent AI hallucination

## Slide 8: Results – Hybrid vs. Simulation​
-
Productivity Gain:
Engineer Time Saved
Faster Verification Cycle
Scalability
Consistency
Limitations
Specification Dependency
Architectural Awareness

## Slide 9: Future Direction
NOW
Prompt-Driven
Formal at Block Level
Prompt‑based synthesis of connectivity and reset assertions
Formal + simulation hybrid
Scalable reuse across FPGA generations
Human‑guided Copilot with verification
oversight
NEXT
Protocol & System
Level Formalization
Build AI-agent to verify every RTL block as protocol‑specific, SVAs, handshakes, corner cases and error cases
Auto‑generate formal summaries and traceable reports to reduce manual analysis of counterexamples
and logs
BEYOND
Cross-Domain &
Multi-Die Verification
Spanning across FPGA–ASIC–SoC–Firmware to ensure reset and HW–SW contract consistency
Inter‑die connectivity and reset propagation for 3D design
Early detection of system‑level integration
failures

## Slide 10: Conclusion
Developed an AI‑assisted formal verification framework for hyperscale FPGA connectivity and reset validation with tool-agnostic
Copilot auto-generated scripts + formal checking + simulation improved coverage, efficiency, and early bug detection
Reduced manual effort and error-prone repetition, increased confidence and boost productivity in first‑silicon bring‑up for cloud FPGA platforms
Demonstrated Effective human‑in‑the‑loop use of LLMs for scalable, higher-assurance and multi-layer verification workflows
Framework is Replicable across FPGA and ASIC projects, addressing growing design complexity

## Slide 11
Thank you
Q & A
Human‑in‑the‑Loop: ENABLED