## Slide 1: Enabling Efficient SpMM for Sparse Attention on GEMM-Optimized Hardware with Block Aggregation
Presenter: | Tianchu Ji
Authors: | Tianchu Ji Niranjan Balasubramanian Michael Ferdman Peter Milder

## Slide 2: Overview
Background
GEMM-optimized hardware requires rigid data flow for best efficiency
Method
Block aggregation: preserve rigid data flow by transforming SpMM to GEMM
sparse attention
Q
KV
SpMM => GEMM tiles
Random data access breaks rigid paths
Problem & Motivation
Sparse attention helps speed up LLMs, but leads to hardware inefficiency
Notes: Our work starts on making a key observation that sparse attention computation in the LLM contradicts with the rigid data path in the existing hardware;
This conflict potentially undermines the frequency, dynamic utilization and throughput of the LLM accelerator.
Our method, named as block aggregation, solves this problem by dynamically collects and aggregates the dense vlues to form small GEMM tiles.
By doing so, the hardware executes SpMM just like computing small tiles of GEMM, thus re-enabling the efficiency of the rigid data path.
Our experiment shows our block aggregation technique achieves higher frequency, throughput and scalability compared to the existing works.

## Slide 3: Problem: attention is compute-intensive Intro
Self-attention pipeline
(Vaswani et al. 2017)
O(n2) complexity
relative to context length
LLMs use increasingly longer context lengths
… leading to much higher computational complexity
Notes: Large Language Models have shown their eye-catching capability on many Natural Language Processing tasks including Machine Translation, Summarization, etc.
To further improve such a capability, recent LLMs intend to support longer context lengths so it can get a broader view of the inputs.
However, this strategy also increases the computational complexity of the LLM.
The main reason is that, the self-attention has a compute intensive GEMM operation.
The runtime of this operation increase quadratically as the context length n grows and finally dominates the runtime of the entire pipeline.
It is vital to optimize this computation to alleviate the computational complexity.

## Slide 4: Sparse attention’s hardware dilemma Background & Motivation
Sparse attention requires hardware for Sparse-Dense Matrix Multiplication (SpMM)
FPGAs can support irregular data access by their customizable logic
But SpMM suffers from inefficiency with GEMM-optimized hardware on FPGA
map to
GEMM-optimized hardware is
inefficient for SpMM
(elements with similar colors belong to same dot-product)
Notes: A well-known technique to optimize the attention computation is to sparsify it.
It has been proven that the attention matrix is moderately sparse, and 80%~90% of its elements can be skipped to save the runtime.
However, it also transform the attention-related computation from GEMM to SpMM and forms irregular data access.
FPGA thus becomes a suitable platform for the sparse attention to efficiently computes irregular SpMM by its customizable logic.
Recent FPGAs begin to equip with special DSPs optimized for GEMM operation, challenging the existing customized SpMM solutions.

## Slide 5: GEMM-optimized Hardware on FPGA Background & Motivation
GEMM-Optimized Hardware with Processing Element (PE) Array
Different PEs share
inputs for data reuse
A large cloud of PEs for faster computation
Achieves high bandwidth by data broadcast
Grouped AI data format (e.g., Intel Block Float, Nvidia Block Scaling)
GEMM-optimized hardware features
Each PE computes a vector dot-product
Notes: As is shown in this figure, GEMM-optimized hardware often contains a large cloud of processing elements (PEs), with each finishing a vector dot-product operation.
Examples can be systolic array such as TPU, or PE array with multi-cycle NoC such as Xilinx AI Engine, and Intel Tensor Blocks.
Such a kind of spatial structure amplifies the input bandwidth (in blue), and requires a highly efficient data path to distribute the matrix elements.
Recent AI hardware also requires sending a block-level scaling factor into the PEs, which further increases the input word size, and eventually the bandwidth of the PEs as well.
To fulfill with large bandwidth requirements, GEMM-optimized hardware tends to reuse and broadcast the data when possible, across the rows and columns of the PE cloud.

## Slide 6: Sparsity is hard on GEMM-optimized Hardware Background & Motivation
GEMM-Optimized Hardware with Processing Element (PE) Array
Rigid data path conflicts with random pattern
The PE array prevents the random access by SpMM:
Notes: Unfortunately, sparse matrix multiplication owns a data access pattern which naturally mismatches with rigid data path, due to 2 major features of the GEMM-optimized hardware:
First, the skipped elements forms a random data access pattern from each PE to the data buffer, and precludes the reusable data access to different PEs.
Second, grouping the elements inside each PE challenges the zero-skipping on the element level.

## Slide 7: Sparsity is hard on GEMM-optimized Hardware Background & Motivation
GEMM-Optimized Hardware with Processing Element (PE) Array
Flexible routing becomes cost-ineffective because:
PE array is so large
(e.g., 237,600 MACs on Intel Stratix® 10 NX)
Grouped inputs are too wide
(e.g., 88-bit word on Intel Stratix® 10 NX)
Notes: Conventional effort to overcome these conflicts is to add flexible data access component to the hardware (in the figure, we use crossbar as an example).
However, since the PE array can scale up to really large, and the grouped inputs grows to many bits, flexible data access can become too complex and finally causes unacceptable frequency degradation or even routing failure.
As a result, on the GEMM-optimized hardware, the existing SpMM solutions become invalid.

## Slide 8: OUR APPROACH keep the data path, regularize the data flow
GEMM-Optimized Hardware with Processing Element (PE) Array
Find GEMM-like tiles in SpMM
Notes: Our observation implies that, the shared data path must be remained to maintain the routability and the frequency of the design.
Instead of adding the cost-inefficient routing logic, we turn to regularize the data flow that can make use of the shared paths.

## Slide 9: Block aggregation: transform SpMM to tiny GEMM Method
Dense attention values form small clusters
Dynamically aggregate the blocks to form GEMM tiles
Q
KV
Existence of locally aggregated attention
Aggregate separated blocks
Notes: Our method to regularize the data flow, is to reconstruct the data access manner of the GEMM for sparse attention computation.
The left figure shows an attention matrix, with dense values (in red) forming vertical and rectangular clusters.
Such a locally aggregated pattern is due to the nature of the attention mechanism.
Based on this, we adopt a new approach by dynamically aggregating the small pieces of the dense attention values into GEMM-like tiles.

## Slide 10: Block aggregation: transform SpMM to tiny GEMM Method
Dense attention values form small clusters
Dynamically aggregate the blocks to form GEMM tiles
Compute the GEMM tiles like a dense matrix
Q
KV
GEMM-optimized hardware
recovers shared paths
Notes: Our solution to this problem, is to reconstruct the data access manner of the GEMM for sparse attention computation.
The left figure shows an attention matrix, with dense values (in red) forming vertical and rectangular clusters.
Such a locally aggregated pattern is due to the nature of the attention mechanism.
Based on this, we adopt a new approach by dynamically aggregating the small pieces of the dense attention values into GEMM-like tiles.

## Slide 11: Block aggregation: uniquify the data requests Method
Combine and uniquify the different data requests from aggregated blocks
Implemented as merge and sort tree in hardware
Aggregated blocks in sparse attention
Notes: Our solution to this problem, is to reconstruct the data access manner of the GEMM for sparse attention computation.
The left figure shows an attention matrix, with dense values (in red) forming vertical and rectangular clusters.
Such a locally aggregated pattern is due to the nature of the attention mechanism.
Based on this, we adopt a new approach by dynamically aggregating the small pieces of the dense attention values into GEMM-like tiles.

## Slide 12: Sparse Attention Core Architecture
Hardware scale:
Up to 138,240 MACs with 288 PEs
480 MACs in each PE
Platform: Intel Stratix® 10 NX with Tensor Blocks
Keeping the rigid data path
Only add an index generator to control data feeding
Notes: Then we proposed our architecture based on a PE array.
The Tensor Block Chain array, in the center of the figure, is the compute core of our hardware.
The PEs inside this array is connected by the broadcast data paths from buffers, exactly the same to the data path organization of the GEMM-optimized hardware.
On top of this GEMM-optimized structure, the only change is that we add the index merging and sorting tree on the upper left, to aggregate the blocks in the sparse attention.

## Slide 13: Sparse Attention Core: Pipeline Architecture
③
③ Multiply the dense matrix blocks
②
② Fetch associated rows from matrix V by indices
②
①
① Aggregate the blocks in attention matrix
Notes: The computation pipeline is finished in 3 steps.
First the index merging and sorting tree aggregates the blocks by their column indices, and provide the indices to serve matrix V fetching
Second, the attention matrix and Value matrix buffer fetches the aggregated block and loads them into the PE array in the center.
Finally the matrix multiplication is performed in the exactly same manner as GEMM computation by the PE array.
We implemented this design on Intel Stratix 10 NX with Tenser Blocks, and evaluated it by the real attention.Value computation from three LLMs on Longbench dataset.

## Slide 14: Higher scalability and frequency Results
Throughput/Frequency compared
with existing SpMM and GEMM hardware
Block aggregation achieves:
  Better scalability
  Higher frequency
than existing SpMM implementation
ours
SIGMA SpMM
(Qin et al. 2020)
Notes: To evaluate the effectiveness of the block aggregation, we first compare the scalability of our design with GEMM design and an existing SpMM design with complex data routing network.
The figure shows the average throughput on the left, and the frequency on the right, of different PE array size on the x axis, respectively.
The throughput comparison on the left shows block aggregation method (in brown) outperforms the GEMM computation (in pink) in terms of the throughput, since it skips the unnecessary computation in the attention.
Compared to the SpMM design which has flexible data routing network, block aggregation method shows a higher throughput, and also manages to extends to a larger scale of PE array.
The right figure shows that usage of the data routing network severely suffers from frequency degradation as the PE array size grows,
while the block aggregation design can keep the same frequency as the dense design, as they are using the same structure of the shared data path.

## Slide 15: Average speedup of 3.13x Results
Average throughput on different models and LongBench (Bai et al. 2024) tasks
(normalized to GEMM on the same hardware and frequency)
Notes: We picked our design with 720 Tensor Blocks and evaluates its throughput normalized to the GEMM, shown in this figure, with eight different tasks on three LLMs.
The average throughput speed up of 2.66x to 3.89x on different models.
Some models, like chatglm2, exhibits a higher throughput than others.

## Slide 16: Conclusion
Problem
Sparse attention leads to hardware inefficiency on GEMM-optimized hardware
Method
Block aggregation: creates GEMM-like tiles from inherently aggregated attentions
Result
3x throughput to GEMM
2.6x throughput to other SpMM and better scalability
Random data access breaks rigid paths
SOURCE CODE
sparse attention
Q
KV
SpMM => GEMM tiles
Notes: Our work starts on making a key observation that sparse attention computation in the LLM contradicts with the rigid data path in the existing hardware;
This conflict potentially undermines the frequency, dynamic utilization and throughput of the LLM accelerator.
Our method, named as block aggregation, solves this problem by dynamically collects and aggregates the dense vlues to form small GEMM tiles.
By doing so, the hardware executes SpMM just like computing small tiles of GEMM, thus re-enabling the efficiency of the rigid data path.
Our experiment shows our block aggregation technique achieves higher frequency, throughput and scalability compared to the existing works.

## Slide 17: Thank you

## Slide 18: Appendix 1 Block Aggregation Explanation

## Slide 19: Aggregating Dense Values into Small Blocks Block Aggregation
Observation: Locally aggregated non-zero values as dense “sub-matrix blocks” - block aggregation
  Reason: some “important” words need attention from other neighboring words:
“What country…?” -> “US”
Compute the matrix multiply of these blocks just like dense matrices
  Why it matters?
Existence of locally aggregated attention
Q
KV
Notes: We can see there is some aggregation pattern in it, vertical-slash pattern is the most common one. Why such localization can help data flow mapping

## Slide 20: Data Access Pattern: Starting from Dense Block Aggregation
Column index defines data access

## Slide 21: Data Access Pattern: A “Bad” Sparse Matrix Block Aggregation
Sparsity creates irregular data access pattern

## Slide 22: Data Access Pattern: A “Good” Sparse Matrix Block Aggregation
More aggregated blocks creates regular access

## Slide 23: More Aggregation = Less Data Access Block Aggregation
More aggregated blocks
= more identical data access
= more shared data path
= high bandwidth utilization

## Slide 24: Block Aggregation in Real Attention Block Aggregation =
More aggregated blocks
= high bandwidth utilization

## Slide 25: Block Aggregation in Real Attention Block Aggregation
It only matters if bubbles are a lot
(which is not true!)
“Bubbles” to regularize the data flow

## Slide 26: Block Aggregation in Real Attention Block Aggregation
Quantitatively analyze sparsity after aggregation
Effective sparsity: Treat this whole sub-block as dense

## Slide 27: Trade-off: sparsity vs. hardware efficiency Block Aggregation
Efficiently organizing data flow is more important on GEMM-optimized hardware for better throughput
sparsity: 43%~77%
sparsity: 80%~90%
Throughput/Frequency compared
with existing SpMM and GEMM hardware
Notes: As discussed before, aggregated blocks in the sparse attention sometimes require bubble insertion to match with the rigid data path, thus leading to lower sparsity.
We evaluated the sparsity degradation caused by the block aggregation.
Although the effective sparsity decreased to 43~77% in average, the speedup it gains from better frequency is still high enough to compensate for that.
Furthermore, allowing such sparsity greatly increases the supported hardware scale.

## Slide 28: Appendix 2 Architecture Details

## Slide 29: Dataflow Mapping: Aggregation Architecture
Col indices are merged and sorted
Step 1: find column index of aggregated blocks by merge&sort, load them into PEs

## Slide 30: Dataflow Mapping: Aggregation Architecture
Step 1: find column index of aggregated blocks by merge&sort, load them into PEs

## Slide 31: Dataflow Mapping: Fetching Architecture
Step 2: find associated row from matrix V column index

## Slide 32: Dataflow Mapping: Fetching Architecture
Step 2: find associated row from matrix V column index

## Slide 33: Dataflow Mapping: Execution Architecture
Step 3: dot-product of loaded Attention blocks and V rows

## Slide 34: Dataflow Mapping: Execution Architecture
Step 3: dot-product of loaded Attention blocks and V rows

## Slide 35: Recap: Bubbles After Aggregation Results
43%–77% average effective sparsity after block aggregation (details in result section)
“Bubbles” to regularize the data flow

## Slide 36: Q: Can it be done on ASIC/GPU?
ASIC - Sure!
GPU - Depending on different memory hierarchy level
  Inside Stream Multiprocessor: need special hardware support
  On Shared Memory level: “shared data paths” becomes “shared memory”
  On system level: might be too coarse grained (less benefit on finding localized data)